## Slide 1: Why model the future?
WEEK 1 OF 15 · STAGE 1: FOUNDATIONS
What an integrated assessment model is and who uses it
New R skill Install R and RStudio; console, scripts, projects, packages
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 1: Why model the future?. What an integrated assessment model is and who uses it. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: Install R and RStudio; console, scripts, projects, packages.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 1 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Explain in plain words what an integrated assessment model (IAM) does
2
Name the main inputs and outputs of an IAM
3
Tell the two model families apart: cost-benefit and process-based
4
Install R and RStudio and run a first script
Big question Climate reports show charts running to 2100. How can anyone say anything about 2100 when we cannot forecast the weather two weeks ahead?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: Climate reports show charts running to 2100. How can anyone say anything about 2100 when we cannot forecast the weather two weeks ahead?

## Slide 4: Who can see 2100?
LET'S START WITH A QUESTION
A weather forecast is unreliable two weeks ahead. Yet climate reports are full of charts that run to 2100.
If nobody can predict the future, what are those charts actually telling us?
Notes: Ask the room for answers before moving on. Some will say 'they are guesses'. Steer toward the key idea of the week: the charts are not forecasts. Each line answers one question: if we assume this, what follows?

## Slide 5: An IAM is like a recipe calculator
AN EVERYDAY PICTURE
You type in the ingredients: how many people, how rich they are, how cheap solar is, which policies exist. The calculator works out a cake that adds up: energy used matches energy made, emissions match fuel burned, warming matches emissions.
What it means for models
1
Inputs are assumptions you choose
2
The model keeps every number consistent
3
Change an ingredient and the cake changes
Notes: Stress the word consistent. The model does not know the future. Its value is that every number agrees with every other number. The analogy breaks in one place: two IAMs given the same ingredients can still bake different cakes, because their equations differ. That is week 12.

## Slide 6: What goes in and what comes out
HOW IT WORKS
1
Inputs
Population, income, technology costs, resources, policies
2
The model
Matches supply and demand, counts emissions
3
Climate
Turns emissions into warming
4
Outputs
Energy mix, emissions, land, prices, temperature
Policies are an input. The model never decides what governments will do; you tell it.
Notes: Point at the first box and say: policies are something you type in, not something the model predicts. Ask students which input they think matters most. Write the answers down and come back to them in week 5.

## Slide 7: Why the word 'integrated'?
KEY POINTS
Energy, economy, land, water and climate sit in one model
A change in one system shows up in the others
Example: more bioenergy means more cropland, which can mean less forest
'Assessment' means the purpose is to inform decisions
So an IAM is a tool for asking what-if questions about this century
Notes: Use the bioenergy example to show why separate models miss things. An energy model alone would call bioenergy clean. A land model alone would not know why farmers plant it. Only together do you see the trade-off.

## Slide 8: Worked example: why consistency matters
WORKED EXAMPLE · STEP BY STEP
Problem The world uses 600 units of energy a year. Each unit releases 0.06 Gt of CO2. A policy cleans up the energy mix so each unit releases 0.03 Gt. How much do emissions fall?
1
Before: 600 × 0.06 = 36 Gt of CO2
2
After: 600 × 0.03 = 18 Gt of CO2
3
Change: 36 − 18 = 18 Gt
4
As a share: 18 ÷ 36 = 0.5, so a 50% cut
Answer
Emissions fall by 18 Gt, a 50% cut (illustrative numbers)
Notes: Do the arithmetic on the board. Then say: an IAM does this bookkeeping for thousands of numbers at once, and it also lets energy use respond to the new prices. The numbers here are illustrative. In the lab students repeat this calculation in R.

## Slide 9: Two families answer different questions
SIDE BY SIDE
 | Cost-benefit models | Process-based models
Question | How much should we cut? | How can a goal be met?
Method | Weigh cutting cost vs damage | Detailed energy and land sectors
Size | A few equations, one world | Thousands of inputs, many regions
Examples | DICE, FUND, PAGE | GCAM, MESSAGEix, REMIND, IMAGE
In this course | Week 5 | Weeks 7 to 13
DICE fits on a page; GCAM has thousands of inputs. Different tools for different questions.
Notes: Students often think 'the model' is one thing. Make the split concrete. DICE gives one global carbon price. GCAM gives an energy mix for each of its 32 regions. We meet DICE first because it is small enough to read in full.

## Slide 10: Quick check
QUICK CHECK · THINK, THEN VOTE
Which question is a job for a process-based model like GCAM?
A
What is one more tonne of CO2 worth in damage?
B
Can Japan reach net zero without new nuclear?
C
Will it rain in Trondheim next Tuesday?
D
What should the global discount rate be?
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: B. It asks how a goal is met, with which technologies, which is the process-based question. A is a cost-benefit question. C is weather, which no IAM does. D is an ethical and economic choice that models take as an input.

## Slide 11: Quick check: answer
QUICK CHECK · ANSWER
Which question is a job for a process-based model like GCAM?
A
What is one more tonne of CO2 worth in damage?
B
Can Japan reach net zero without new nuclear?
C
Will it rain in Trondheim next Tuesday?
D
What should the global discount rate be?
Notes: Answer: B. It asks how a goal is met, with which technologies, which is the process-based question. A is a cost-benefit question. C is weather, which no IAM does. D is an ethical and economic choice that models take as an input.

## Slide 12: IAMs sit behind big decisions
NUMBERS TO REMEMBER
~1,200
what-if pathways in the IPCC's 2022 mitigation report
5
lecture days in NTNU's EP8900 course, which inspired this one
15
weeks for us to go from zero to running GCAM
IPCC = Intergovernmental Panel on Climate Change, the UN body that assesses climate research.
Notes: The IPCC Working Group III report from 2022 sorted about 1,200 pathways from many models. Check the exact count against the AR6 Working Group III report before teaching. IAM results are also used in national climate plans and by companies and investors.

## Slide 13: Who uses IAM results?
KEY IDEA
1
IPCC reports
Pathways that limit warming to 1.5 °C or 2 °C come from IAMs.
2
Governments
National climate plans test targets such as net zero by 2050 with IAMs.
3
Companies and investors
Banks and firms use IAM scenarios to stress-test their plans.
4
Researchers
To explore trade-offs between energy, food, water and climate.
Notes: Ask if anyone has seen an IAM result without knowing it. The common answer is the IPCC 1.5 °C pathways in the news. Mention that the central-bank climate scenarios (NGFS) also come from IAMs, including GCAM.

## Slide 14: Common mix-ups
WATCH OUT
Not quite
Better
"The model predicts 2.7 °C by 2100."
It says what follows if its assumptions hold. Change the assumptions and the number changes.
Process-based models tell us how much to cut.
They show how a chosen goal could be met. 'How much' is the cost-benefit question.
An IAM decides which policies governments adopt.
Policies are an input you choose. The model works out what follows from them.
Notes: The first mix-up appears in news stories all the time. Ask students to rephrase a headline such as 'models predict 3 °C' into correct IAM language: 'if current policies continue, models find about 3 °C'.

## Slide 15: Your first R script
IN R
<- stores a value under a name
c() combines values into a vector
A line starting with # is a note for humans
install.packages("tidyverse") # once per computer
library(tidyverse) # every session
co2 <- c(before = 280, today = 420) # ppm
co2["today"] - co2["before"] # 140
co2["today"] / co2["before"] # 1.5
Notes: 280 ppm is the CO2 level before industrialisation, and today it is about 420 ppm. ppm means parts per million. The script shows the rise is 140 ppm, or 1.5 times the old level. In the lab students type this themselves.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Integrated assessment model A computer model that links energy, the economy, land and climate, so we can ask what-if questions about the future. Short form: IAM.
Scenario A consistent what-if story about the future, with numbers attached. It is not a forecast.
Cost-benefit model An IAM that weighs the cost of cutting emissions against the damage avoided, in a few equations. Example: DICE.
Process-based model An IAM that represents energy and land sectors in detail to show how a goal could be met. Examples: GCAM, MESSAGEix.
R package A bundle of ready-made R functions. Install it once per computer, load it with library() in every session.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 1: En-ROADS and your first R script
HANDS-ON LAB
Try climate policies in the En-ROADS simulator, then install R and RStudio and run a first script.
Script: labs/lab1.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Try climate policies in the En-ROADS simulator, then install R and RStudio and run a first script. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Play with En-ROADS
LAB · STEP 1 OF 4
1
Open en-roads.climateinteractive.​org. Move the sliders (carbon price, renewables, coal) and watch the 2100 temperature change. Note one question it cannot answer.
Notes: Spend about 40 minutes here. Collect the questions En-ROADS cannot answer, such as which technology in which region, or land and water trade-offs. Keep the list for week 7; those questions are why GCAM exists.

## Slide 19: Install R and RStudio
LAB · STEP 2 OF 4
2
Install R first, then RStudio. In RStudio make a new project called iam-course. Every lab lives in this project folder.
Notes: Installation always takes longer than planned. Keep the installers on a USB stick in case the network is slow. Nobody should leave without a working setup or a booked drop-in slot.

## Slide 20: Install and load a package
LAB · STEP 3 OF 4
Install the tidyverse once. Load it with library() at the top of every script.
install.packages("tidyverse") # once per computer
library(tidyverse) # every session
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: Installing the tidyverse can take several minutes. Start it early and explain project folders while it runs.

## Slide 21: Run your first calculation
LAB · STEP 4 OF 4
Open a new script, type these lines, and run them with Ctrl+Enter. Typing teaches more than pasting.
# CO2 in the air, parts per million
co2 <- c(before = 280, today = 420)
co2["today"] - co2["before"] # expect 140
co2["today"] / co2["before"] # expect 1.5
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: Name three ideas out loud: the arrow stores a value under a name, c() combines values into a vector, and a hash starts a comment. If they see 140 and 1.5, the setup works.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
You moved at least three En-ROADS sliders and noted the 2100 temperature
R prints 140 and 1.5
Your script is saved inside the iam-course project
Worksheet questions
1
Write one question En-ROADS answered and one it could not answer.
2
Add three words to the class glossary with a one-line definition each.
3
Change the script to use 2.6 ppm per year of growth: how many ppm after 10 more years?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
An IAM links energy, economy, land and climate to answer what-if questions
2
Its results are scenarios, not forecasts: if this, then that
3
Policies are an input you choose, not something the model predicts
4
Cost-benefit models ask 'how much'; process-based models ask 'how'
Next: week 2
Week 2 opens the climate box: how CO2 becomes warming, and why the total emitted matters most.
Practise
Interactive course, week 1: try the warming explorer and the 5-question quiz.
Readings: Carbon Brief (2018), Q&A: How 'integrated assessment models' are used to study climate change; R for Data Science (free online): introduction
Notes: Go back to the goals from the start: Explain in plain words what an integrated assessment model (IAM) does; Name the main inputs and outputs of an IAM; Tell the two model families apart: cost-benefit and process-based; Install R and RStudio and run a first script. Ask students to rate themselves on each. Then point to next week: Week 2 opens the climate box: how CO2 becomes warming, and why the total emitted matters most.