## Slide 1: Climate primer
WEEK 2 OF 15 · STAGE 1: FOUNDATIONS
How CO2 becomes warming, and why the total matters
New R skill Vectors and data frames; reading CSV files; a first ggplot2 chart
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 2: Climate primer. How CO2 becomes warming, and why the total matters. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: Vectors and data frames; reading CSV files; a first ggplot2 chart.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 2 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Trace the four steps from emissions to temperature
2
Explain why warming follows the running total of CO2
3
Work out how long a carbon budget lasts
4
Read a CSV file into R and draw a first chart with ggplot2
Big question Does a tonne of CO2 burned in 1960 still matter today?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: Does a tonne of CO2 burned in 1960 still matter today?

## Slide 4: Does old CO2 still count?
LET'S START WITH A QUESTION
A tonne of CO2 burned in 1960 still warms the planet today about as much as a tonne burned this morning.
If that is true, what kind of limit does a temperature target set on our emissions?
Notes: Let students guess. The answer we are building towards: the climate cares about the total emitted, not when. So a temperature limit becomes a fixed allowance, like a bank balance. That allowance is the carbon budget.

## Slide 5: The atmosphere is a bathtub
AN EVERYDAY PICTURE
The tap is the CO2 we emit each year. The plug hole is small: oceans and forests take up some CO2, but a little under half of each year's emissions stays in the air. The water level keeps rising as long as the tap runs faster than the drain.
What it means for models
1
Tap = yearly emissions
2
Water level = CO2 in the air
3
Only turning the tap (almost) off stops the rise
Notes: This is the single most useful picture of the week. Ask: if we turn the tap down by half, does the level fall? No, it still rises, just more slowly. That answers the most common beginner mistake before it happens.

## Slide 6: From emissions to temperature in four steps
HOW IT WORKS
1
1 Emissions
Fossil fuels and land clearing release CO2 each year
2
2 Concentration
A little under half stays in the air: 280 to over 420 ppm
3
3 Forcing
Extra CO2 traps heat, measured in W/m²
4
4 Temperature
The surface warms until energy in and out balance
Steps 2 to 4 are what the Hector model calculates. GCAM hands its emissions to Hector in week 10.
Notes: Every IAM has some version of this chain. Cost-benefit models like DICE squeeze it into a few equations. GCAM passes its emissions to Hector, a simple climate model. In the lab students run Hector themselves and see step 4 respond.

## Slide 7: Warming tracks the running total of CO2
PICTURE THE NUMBERS
Chart: CO2 emitted from 2020 onward (GtCO2)
| 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000
Extra warming (°C) | 0 | 0.225 | 0.45 | 0.675 | 0.9 | 1.125 | 1.35
Computed from ΔT ≈ 0.45 °C × cumulative CO2 ÷ 1,000 Gt
Read it like this
1
Each 1,000 GtCO2 adds about 0.45 °C
2
A straight line: no 'safe' emissions that do not count
3
Warming stops rising only at net zero
Notes: Scientists find that warming plotted against total CO2 emitted is close to a straight line. The slope of about 0.45 °C per 1,000 Gt is a central estimate; check the AR6 Working Group I value before teaching. This line is why every serious temperature target ends at net zero.

## Slide 8: Two carbon budgets to remember
NUMBERS TO REMEMBER
500 Gt
CO2 from 2020 for a 50% chance of 1.5 °C
1,150 Gt
CO2 from 2020 for a 67% chance of 2 °C
~40 Gt
CO2 the world emits each year
Budgets from IPCC AR6 Working Group I (2021), counted from the start of 2020; part is already used.
Notes: These budgets are quoted from memory; check them against the AR6 Working Group I Summary for Policymakers before teaching. Ask students: if 500 Gt is the budget and we emit 40 a year, roughly how long does it last? Answer on the next slide.

## Slide 9: Worked example: how long does 500 Gt last?
WORKED EXAMPLE · STEP BY STEP
Problem The 1.5 °C budget is 500 GtCO2. The world emits about 40 Gt a year. How long does the budget last?
1
If emissions stay flat: 500 ÷ 40 = 12.5 years, then a sudden stop
2
If they fall in a straight line to zero over T years, the total is a triangle
3
Triangle area = ½ × 40 × T
4
Set it equal to the budget: ½ × 40 × T = 500, so 20T = 500
5
T = 500 ÷ 20 = 25 years
Answer 12.5 years if flat; 25 years with a steady straight-line decline
Notes: Draw both shapes on the board. A straight-line decline buys twice the time of a cliff edge, but the line has to reach zero either way. This is why 1.5 °C pathways reach net-zero CO2 around mid-century.

## Slide 10: Same budget, two shapes
PICTURE THE NUMBERS
Chart: Years from now
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20 | 22.5 | 25
Flat, then stop | 40 | 40 | 40 | 40 | 40 | 0 | 0 | 0 | 0 | 0 | 0
Straight line down | 40 | 36 | 32 | 28 | 24 | 20 | 16 | 12 | 8 | 4 | 0
Illustrative paths for the 500 Gt budget at 40 Gt a year
Read it like this
1
The area under each line is the CO2 emitted
2
Both areas equal 500 Gt
3
Both end at zero
Notes: Ask which path is more realistic. Nobody can switch off the world economy in one year, so real pathways look like the second line, or curve more gently. The point is that the budget fixes the area, and the area has to end at zero.

## Slide 11: Quick check
QUICK CHECK · THINK, THEN VOTE
The 2 °C budget is 1,150 GtCO2. At 40 Gt a year, how long does it last if emissions stay flat?
A
About 12 years
B
About 29 years
C
About 58 years
D
About 115 years
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: 1,150 ÷ 40 = 28.75, about 29 years. Follow-up: if emissions fall in a straight line, ½ × 40 × T = 1,150 gives T = 57.5 years, the third option. Students who chose C answered the follow-up question.

## Slide 12: Quick check: answer
QUICK CHECK · ANSWER
The 2 °C budget is 1,150 GtCO2. At 40 Gt a year, how long does it last if emissions stay flat?
A
About 12 years
B
About 29 years
C
About 58 years
D
About 115 years
Notes: Answer: 1,150 ÷ 40 = 28.75, about 29 years. Follow-up: if emissions fall in a straight line, ½ × 40 × T = 1,150 gives T = 57.5 years, the third option. Students who chose C answered the follow-up question.

## Slide 13: Two numbers people mix up
COMPARE
Emissions
What we add each year
Measured in Gt of CO2 per year
About 40 Gt per year today
The tap in the bathtub
Concentration
What is in the air now
Measured in parts per million (ppm)
About 280 before industry, over 420 today
The water level in the bathtub
Notes: Emissions are a flow, concentration is a stock. A news headline saying 'emissions fell, so CO2 levels will fall' confuses the two. Concentration keeps rising as long as emissions are above what nature removes.

## Slide 14: Common mix-ups
WATCH OUT
Not quite
Better
Halve emissions and you halve warming.
Halving the yearly rate only slows the rise. Warming stops rising only at net zero.
ppm and Gt per year measure the same thing.
ppm is what is in the air (the level). Gt per year is what we add (the tap).
500 Gt of CO2 gives 1.5 °C of warming on its own.
It gives about 0.225 °C more. We are already near 1.1 °C, and room is kept for methane and other gases.
Notes: The third point confuses even strong students. 0.45 × 500 ÷ 1,000 = 0.225 °C of extra CO2 warming, on top of the warming that has already happened. The budget is what is left once other gases are counted.

## Slide 15: Your first chart in R
IN R
A data frame is a table; each column is a vector
$ picks one column out of a table
Every ggplot: data, aes (what goes on which axis), a geom
co2 <- read_csv("data/co2_annual.csv")
glimpse(co2)
max(co2$ppm)
ggplot(co2, aes(x = year, y = ppm)) +
geom_line() +
labs(y = "CO2 (ppm)")
Notes: Every ggplot has the same three parts. Ask students to swap geom_line for geom_point to see that only the last part changes. Remind them that file paths start from the project folder, which is why we made a project in lab 1.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Concentration How much CO2 is in the air, measured in parts per million (ppm). About 280 before industry, over 420 today.
Radiative forcing Extra heat trapped by greenhouse gases, measured in watts per square metre (W/m²). A thicker 'blanket'.
Cumulative emissions All the CO2 emitted added up over the years: the running total.
Carbon budget The total CO2 that can still be emitted while keeping warming below a chosen limit.
Net zero The point where CO2 added to the air each year is balanced by CO2 removed, so the running total stops growing.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 2: first plots and the Hector climate model
HANDS-ON LAB
Read a CO2 data file and plot it, then run the Hector climate model for a low and a high emissions path and compare the temperatures.
Script: labs/lab2.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Read a CO2 data file and plot it, then run the Hector climate model for a low and a high emissions path and compare the temperatures. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Read and look at the data
LAB · STEP 1 OF 4
read_csv() loads a table. glimpse() and head() show what is inside before you plot anything.
library(tidyverse)
co2 <- read_csv("data/co2_annual.csv")
glimpse(co2)
head(co2)
max(co2$ppm)
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: The file has two columns, year and ppm. If read_csv cannot find the file, the project is not open or the file is not in the data folder.

## Slide 19: Draw the CO2 chart
LAB · STEP 2 OF 4
Map year to x and ppm to y, then draw a line.
ggplot(co2, aes(x = year, y = ppm)) +
geom_line() +
labs(y = "CO2 (ppm)")
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: Ask students to describe the shape in one sentence. It should rise faster in recent decades.

## Slide 20: Run Hector for a low path
LAB · STEP 3 OF 4
Hector is the simple climate model inside GCAM. newcore() sets it up, run() runs it, fetchvars() pulls out temperature.
library(hector)
ini <- system.file("input/hector_ssp126.ini",
package = "hector")
low <- newcore(ini, name = "low")
run(low)
t_low <- fetchvars(low, 2000:2100,
GLOBAL_TAS())
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: SSP1-2.6 is a strong-mitigation path; the labels are explained in week 6. Older Hector versions call the variable GLOBAL_TEMP(); test the script before class.

## Slide 21: Run a high path and compare
LAB · STEP 4 OF 4
Repeat with SSP5-8.5, stack the two results and colour the lines by scenario.
ini <- system.file("input/hector_ssp585.ini",
package = "hector")
high <- newcore(ini, name = "high")
run(high)
t_high <- fetchvars(high, 2000:2100,
GLOBAL_TAS())
temps <- bind_rows(t_low, t_high)
ggplot(temps, aes(year, value,
colour = scenario)) +
geom_line()
Notes: fetchvars returns columns scenario, year, variable, value and units, which is why it plots directly. The two lines should be close until about 2040 and then separate.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
Your CO2 chart rises over time and ends above 400 ppm
The two Hector lines are close until about 2040, then split
By 2100 the high path is several degrees warmer than the low path
Worksheet questions
1
Why do the two temperature paths differ so little by 2050? Use the idea of cumulative emissions.
2
What is the highest CO2 value in the file, and in which year?
3
Change geom_line() to geom_point(). What changed and what stayed the same?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
Emissions raise CO2 in the air, which traps heat (forcing), which warms the surface
2
Warming follows the running total of CO2: about 0.45 °C per 1,000 Gt
3
So a temperature limit becomes a carbon budget, and warming stops only at net zero
4
In R: read_csv() loads a table, ggplot() + aes() + a geom draws it
Next: week 3
Week 3 asks where the emissions come from: energy, and the four factors of the Kaya identity.
Practise
Interactive course, week 2: try the budget explorer and the 5-question quiz.
Readings: IPCC AR6 Working Group I (2021), Summary for Policymakers: sections on carbon budgets; R for Data Science: data visualisation chapter
Notes: Go back to the goals from the start: Trace the four steps from emissions to temperature; Explain why warming follows the running total of CO2; Work out how long a carbon budget lasts; Read a CSV file into R and draw a first chart with ggplot2. Ask students to rate themselves on each. Then point to next week: Week 3 asks where the emissions come from: energy, and the four factors of the Kaya identity.