## Slide 1: Energy primer
WEEK 3 OF 15 · STAGE 1: FOUNDATIONS
Where emissions come from, in four numbers
New R skill dplyr: filter, select, mutate, group_by, summarise; the pipe
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 3: Energy primer. Where emissions come from, in four numbers. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: dplyr: filter, select, mutate, group_by, summarise; the pipe.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 3 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Follow energy from primary source to the service people want
2
Write the Kaya identity and explain each of its four factors
3
Use ratios to see which factor drove a country's emissions
4
Use dplyr verbs and the pipe to filter and compute new columns
Big question The CO2 from eight billion people's daily choices can be written as four numbers multiplied together. Which ones can policy change?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: The CO2 from eight billion people's daily choices can be written as four numbers multiplied together. Which ones can policy change?

## Slide 4: Four numbers behind all CO2
LET'S START WITH A QUESTION
The CO2 from eight billion people's daily choices can be written as four numbers multiplied together. Two of them we hope will keep rising.
If population and income keep growing, what must happen to the other two?
Notes: Do not reveal the four numbers yet. Ask students which two we hope will rise: more people living longer and people getting richer. Then climate policy has to push the other two down faster than those rise.

## Slide 5: Energy is like water through leaky pipes
AN EVERYDAY PICTURE
Water leaves a reservoir, passes a treatment plant, flows through pipes and comes out of your tap. Some is lost at every stage. Energy is the same: coal or sunlight is turned into electricity, sent through wires, and finally lights your desk.
What it means for models
1
You do not want energy, you want the service
2
Some energy is lost at each step
3
Two levers: cleaner supply, or less energy per service
Notes: The service is what people actually want: a warm room, a lit desk, a trip to work. This idea matters because process-based IAMs follow the whole chain and can compare a solar farm with a better-insulated building.

## Slide 6: From resource to service in four steps
HOW IT WORKS
1
Primary
Coal, oil, gas, uranium, sun, wind, biomass
2
Conversion
Power plants and refineries make usable forms
3
Final
Electricity, fuels and heat delivered to users
4
Services
Warm rooms, light, travel, steel, cement
Clean up the left side (supply), or need less energy for the same service (right side).
Notes: Give one worked example aloud: a litre of petrol becomes kilometres travelled. A more efficient car gives more kilometres from the same litre. That is a change on the right side of the chain.

## Slide 7: Worked example: losses along the chain
WORKED EXAMPLE · STEP BY STEP
Problem Start with 100 units of coal. The power plant is 40% efficient and the grid loses 10%. How much reaches homes?
1
Power plant: 100 × 0.40 = 40 units of electricity
2
Grid: 40 × 0.90 = 36 units reach homes
3
Lost: 100 − 36 = 64 units, about two thirds
4
So 1 unit saved at home saves 100 ÷ 36 ≈ 2.8 units of coal
Answer
36 units reach homes; saving 1 unit at home saves about 2.8 units of coal
Notes: Illustrative efficiencies, but realistic for an older coal plant. The last line is the punchline: saving electricity at the socket saves nearly three times as much primary energy.

## Slide 8: The Kaya identity
KEY POINTS
CO2 = P × (G ÷ P) × (E ÷ G) × (C ÷ E)
P = population; G = GDP (the size of the economy)
G ÷ P = income per person
E ÷ G = energy intensity; C ÷ E = carbon intensity
Each top cancels the bottom of the next, so it is always true
Notes: This is an identity, not a theory. The terms cancel to leave CO2 = C. Its value is as a way of organising data. Warn students that the factors are not independent; for example, richer countries often have lower energy intensity.

## Slide 9: Worked example: a country called Avalon
WORKED EXAMPLE · STEP BY STEP
Problem Avalon (invented) has 100 million people, $1,000 billion GDP, 10 EJ of energy and 600 Mt of CO2. What are its four factors?
1
Income: $1,000 bn ÷ 100 m = $10,000 per person
2
Energy intensity: 10 EJ ÷ $1,000 bn = 10 MJ per dollar
3
Carbon intensity: 600 Mt ÷ 10 EJ = 60 kg CO2 per GJ
4
Check: 100 m × $10,000 × 10 MJ/$ × 0.06 kg/MJ = 600 Mt
Answer
Income $10,000; 10 MJ per $; 60 kg CO2 per GJ. The pieces rebuild 600 Mt.
Notes: EJ is exajoule, a huge amount of energy; MJ is megajoule. Students do not need to memorise units. What matters is the check in the last line: multiply the factors and you get back the total. That same check is built into the lab.

## Slide 10: Avalon 30 years later: what drove CO2?
PICTURE THE NUMBERS
Chart: Kaya factor
| Population | Income | Energy/GDP | CO2/energy | CO2
Ratio: year 30 ÷ year 0 | 1.2 | 1.5 | 0.7 | 0.8 | 1.008
Invented numbers. Lab 3 makes this chart for a real country.
Read it like this
1
Population ×1.2 and income ×1.5 pushed CO2 up
2
Energy intensity ×0.7 and carbon intensity ×0.8 pulled it down
3
1.2 × 1.5 × 0.7 × 0.8 = 1.008: almost flat
Notes: Bars above 1 pushed emissions up, bars below 1 pulled them down. Efficiency and cleaner energy just cancelled growth in people and income. Ask: which two bars can policy move most directly? The last two.

## Slide 11: Quick check
QUICK CHECK · THINK, THEN VOTE
Over 20 years: population ×1.1, income ×2.0, energy intensity ×0.6, carbon intensity ×0.9. What happens to CO2?
A
Falls by about 10%
B
Stays the same
C
Rises by about 19%
D
Doubles
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: 1.1 × 2.0 × 0.6 × 0.9 = 2.2 × 0.54 = 1.188, so CO2 rises by about 19%. Students who add the percentages (+10 +100 −40 −10 = +60%) get the wrong answer. That is the trap on the next slide.

## Slide 12: Quick check: answer
QUICK CHECK · ANSWER
Over 20 years: population ×1.1, income ×2.0, energy intensity ×0.6, carbon intensity ×0.9. What happens to CO2?
A
Falls by about 10%
B
Stays the same
C
Rises by about 19%
D
Doubles
Notes: Answer: 1.1 × 2.0 × 0.6 × 0.9 = 2.2 × 0.54 = 1.188, so CO2 rises by about 19%. Students who add the percentages (+10 +100 −40 −10 = +60%) get the wrong answer. That is the trap on the next slide.

## Slide 13: Common mix-ups
WATCH OUT
Not quite
Better
Add the percentage changes: +20%, +50%, −30%, −20% gives +20%.
Kaya factors multiply: 1.2 × 1.5 × 0.7 × 0.8 = 1.008, only +0.8%.
Energy intensity and carbon intensity are the same thing.
Energy intensity is energy per dollar (efficiency). Carbon intensity is CO2 per unit of energy (clean supply).
Kaya explains why emissions changed.
It describes how they changed. The causes behind each factor need a model.
Notes: Adding percentages works only for very small changes. The third point is subtle: Kaya is bookkeeping. GCAM is what explains why energy intensity fell, through prices and technology choices.

## Slide 14: The pipe: read it as 'and then'
IN R
filter keeps rows; select keeps columns
mutate makes new columns from old ones
== compares; a single = assigns
mine <- kaya |>
filter(country == "Japan") |>
select(year, pop, gdp, energy, co2) |>
mutate(
income = gdp / pop,
e_intens = energy / gdp,
c_intens = co2 / energy
)
Notes: Read the block aloud: take kaya, and then keep Japan, and then keep five columns, and then add three new ones. Build it one line at a time in the lab, running after each line, so beginners see which line breaks.

## Slide 15: Words to add to the class glossary
NEW WORDS THIS WEEK
Primary energy Energy as found in nature before conversion: coal, oil, gas, uranium, sunlight, wind, biomass.
Final energy Energy delivered to users after conversion: electricity, petrol, heat.
Energy intensity Energy used per dollar of GDP. Falls when the economy becomes more efficient.
Carbon intensity CO2 released per unit of energy. Falls when energy comes from cleaner sources.
Kaya identity CO2 = population × income per person × energy intensity × carbon intensity. Always true by arithmetic.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 16: Lab 3: Kaya decomposition with dplyr
HANDS-ON LAB
Break one country's emissions into population, income, energy intensity and carbon intensity, and find which factor drove the change.
Script: labs/lab3.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Break one country's emissions into population, income, energy intensity and carbon intensity, and find which factor drove the change. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 17: Pick a country and compute factors
LAB · STEP 1 OF 4
Replace Japan with your own country. Run after each line so you can see what changed.
kaya <- read_csv("data/kaya_data.csv")
mine <- kaya |>
filter(country == "Japan") |>
select(year, pop, gdp, energy, co2) |>
mutate(
income = gdp / pop,
e_intens = energy / gdp,
c_intens = co2 / energy
)
Notes: Ask each student to choose a different country before the lab starts and write it on the board. The comparison across the room at the end is the payoff.

## Slide 18: Compare the last year with the first
LAB · STEP 2 OF 4
summarise() turns many rows into one. last() ÷ first() gives the ratio for each factor.
change <- mine |>
arrange(year) |>
summarise(
pop = last(pop) / first(pop),
income = last(income) / first(income),
e_intens = last(e_intens) / first(e_intens),
c_intens = last(c_intens) / first(c_intens),
co2 = last(co2) / first(co2)
)
change
Notes: A ratio above 1 means that factor grew. Ask students to say aloud which factor grew most.

## Slide 19: Check the identity
LAB · STEP 3 OF 4
The four ratios must multiply to the CO2 ratio. If they do not, there is a typo somewhere.
change$pop * change$income *
change$e_intens * change$c_intens
change$co2
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: This is a built-in test. Because Kaya always holds, the two numbers must match. A mismatch almost always means a misspelt column in mutate.

## Slide 20: Three countries at once
LAB · STEP 4 OF 4
%in% keeps several countries. group_by(country) makes summarise work once per country.
kaya |>
filter(country %in% c("Japan", "India", "Brazil")) |>
mutate(income = gdp / pop,
e_intens = energy / gdp,
c_intens = co2 / energy) |>
arrange(year) |>
group_by(country) |>
summarise(co2 = last(co2) / first(co2),
income = last(income) / first(income))
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: This is a shortened version of step 4 in lab3.R; the full script summarises all five ratios. Expect income to dominate in fast-growing economies, while falling energy intensity is common almost everywhere.

## Slide 21: Did it work?
LAB · CHECK YOUR WORK
You should see
Your four factor ratios multiply to the CO2 ratio
You can name the factor that grew most in your country
The three-country table has one row per country
Worksheet questions
1
Which Kaya factor rose most in your country, and which fell most?
2
Explain in two sentences why adding the percentage changes gives the wrong answer.
3
Compare your country with a neighbour's: which lever (efficiency or clean energy) did each rely on?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 22: Take-home messages
RECAP
1
Energy flows from primary sources through conversion to the services people want, with losses
2
Kaya: CO2 = population × income × energy intensity × carbon intensity
3
The factors multiply, so compare ratios, not added percentages
4
Policy mainly works on the last two: efficiency and clean energy
Next: week 4
Week 4 adds the economics: how prices balance markets, what a carbon price does, and why the future gets discounted.
Practise
Interactive course, week 3: try the kaya explorer and the 5-question quiz.
Readings: IPCC AR6 Working Group III (2022), Summary for Policymakers: section on emissions trends and drivers; R for Data Science: data transformation chapter
Notes: Go back to the goals from the start: Follow energy from primary source to the service people want; Write the Kaya identity and explain each of its four factors; Use ratios to see which factor drove a country's emissions; Use dplyr verbs and the pipe to filter and compute new columns. Ask students to rate themselves on each. Then point to next week: Week 4 adds the economics: how prices balance markets, what a carbon price does, and why the future gets discounted.