## Slide 1: The energy system in GCAM
WEEK 8 OF 15 · STAGE 2: GCAM IN DEPTH
Change one cost and follow the ripples
New R skill Comparing scenarios: differences from reference with a join; rchart for standard GCAM charts
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 8: The energy system in GCAM. Change one cost and follow the ripples. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: Comparing scenarios: differences from reference with a join; rchart for standard GCAM charts.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 8 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Trace energy from resources through power plants and refineries to final demand
2
Calculate a technology's levelised cost from its three parts
3
Explain why new investment changes fast but the whole fleet changes slowly
4
Run a scenario with an add-on file and compute differences from Reference in R
Big question If solar power becomes much cheaper, how fast does the electricity mix change, and why not overnight?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: If solar power becomes much cheaper, how fast does the electricity mix change, and why not overnight?

## Slide 4: Solar gets cheaper tomorrow. What happens?
LET'S START WITH A QUESTION
Suppose new solar panels suddenly cost the same as coal. Your region's power plants are mostly coal and gas today.
How long until most of the electricity comes from solar: 5 years, 20 years, or longer?
Notes: Collect guesses and write them on the board. Most students guess fast change. By the end of the lecture they will be able to calculate why the whole fleet changes much more slowly than new investment. The lab tests the guess with the CheapSolar scenario.

## Slide 5: Energy moves along three conveyor belts
AN EVERYDAY PICTURE
Think of an engine hall with three belts. The first carries raw resources: oil barrels, coal, sunlight and wind. The second runs through power stations, refineries and hydrogen plants. The third delivers to homes, lorries and steel mills. Every handover between belts is a market with a price.
What it means for models
1
Belt 1: resources (primary energy)
2
Belt 2: transformation (electricity, fuels, hydrogen)
3
Belt 3: final demand in buildings, transport and industry
Notes: This is stop two of the study guide memory route, the engine hall. Link back to week 3: primary, secondary and final energy are the three belts. Demand for services pulls fuel along the belts, so read the chain right to left as cause.

## Slide 6: Demand for services pulls energy through the system
HOW IT WORKS
1
Resources
Oil, gas, coal, uranium, wind, sun, biomass
2
Transformation
Power plants, refineries, hydrogen production
3
Final energy
Electricity, liquid fuels, gas, hydrogen delivered
4
Services
Warm homes, kilometres travelled, tonnes of steel
Fossil resources are graded: the cheap grades are used first, so extraction cost rises over time
Notes: Industry has six manufacturing sectors: iron and steel, chemicals, aluminium, cement, fertiliser and other industry, plus food processing, construction, mining and farm energy use (Source: GCAM v8.2 documentation, Energy Demand page). Hydrogen is a future commodity with no use in the base years. GCAM works out the last two Kaya factors, energy intensity and carbon intensity, from these markets.

## Slide 7: Worked example: what does gas power cost?
WORKED EXAMPLE · STEP BY STEP
Problem Levelised cost = non-energy cost + fuel price ÷ efficiency + carbon price × emissions per MWh. Gas plant, 50% efficient, carbon price $50/t.
1
Non-energy cost (building and running the plant): $20 per MWh
2
Fuel: gas at $25 per MWh ÷ 0.5 efficiency = $50
3
Emissions: 0.2 t per MWh of gas ÷ 0.5 = 0.4 t per MWh of electricity
4
Carbon cost: 0.4 × $50 = $20
5
Total: 20 + 50 + 20 = $90 per MWh
Answer $90 per MWh, the same as week 4's gas cost with a $50 carbon price
Notes: Week 4's table was this formula in disguise. Only the first term is an input you set directly; the fuel price comes from the gas market and the carbon price from the policy. That is why one cost change ripples through the model. Numbers are illustrative.

## Slide 8: Three parts of cost, three different sources
SIDE BY SIDE
Part of cost | Where it comes from | Example change
Non-energy cost | Input file, per technology and year | CheapSolar lowers it
Fuel ÷ efficiency | The fuel market, solved by GCAM | A gas shortage raises it
Carbon price × emissions | The policy you add | CarbonPrice in week 10
Future costs and efficiencies are assumptions written in input files before the run
Notes: The point to land: GCAM does not discover that solar gets cheaper. You tell it so in the input files. A result where cheap solar wins partly restates your assumption, which is why the report must state every assumption it changed.

## Slide 9: Quick check
QUICK CHECK · THINK, THEN VOTE
Coal plant: non-energy $25/MWh, coal $14/MWh, 40% efficient, 0.36 tCO2 per MWh of coal. Cost at $50/t?
A
$75
B
$85
C
$105
D
$120
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: $105. Fuel 14 / 0.4 = 35. Emissions 0.36 / 0.4 = 0.9 t per MWh of electricity, times 50 = 45. Total 25 + 35 + 45 = 105, which is week 4's coal number with the tax. This is the study guide's try-it question for week 8.

## Slide 10: Quick check: answer
QUICK CHECK · ANSWER
Coal plant: non-energy $25/MWh, coal $14/MWh, 40% efficient, 0.36 tCO2 per MWh of coal. Cost at $50/t?
A
$75
B
$85
C
$105
D
$120
Notes: Answer: $105. Fuel 14 / 0.4 = 35. Emissions 0.36 / 0.4 = 0.9 t per MWh of electricity, times 50 = 45. Total 25 + 35 + 45 = 105, which is week 4's coal number with the tax. This is the study guide's try-it question for week 8.

## Slide 11: Worked example: CheapSolar's new investment
WORKED EXAMPLE · STEP BY STEP
Problem Before: coal $60, gas $70, solar $80, exponent −4 gave 54 / 29 / 17. CheapSolar makes solar cost $60.
1
Coal: 60^−4 = 7.72 × 10^−8
2
Solar now also 60^−4 = 7.72 × 10^−8
3
Gas: 70^−4 = 4.16 × 10^−8
4
Sum = 7.72 + 7.72 + 4.16 = 19.6 (× 10^−8)
5
Shares: 7.72 ÷ 19.6 = 39%, gas 4.16 ÷ 19.6 = 21%
Answer Coal 39%, gas 21%, solar 39% of new investment
Notes: Solar jumps from 17 to 39 percent of new investment. Gas and coal both lose a little and neither drops to zero, which is the logit rule from week 7. Illustrative numbers, not GCAM results.

## Slide 12: New investment jumps; the whole fleet creeps
PICTURE THE NUMBERS
Chart: Years after solar becomes cheaper
| 0 | 5 | 10 | 15 | 20 | 25 | 30
Solar share of new investment | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4
Solar share of whole fleet | 10 | 15.9 | 20.6 | 24.3 | 27.4 | 29.8 | 31.7
Illustrative fleet: solar starts at 10%, 20% replaced per period
Read it like this
1
Each 5 years, 20% of the fleet retires and is replaced
2
Next fleet share = 0.8 × old + 0.2 × 39.4%
3
After 30 years solar is still under a third
Notes: Work the first step aloud: 0.8 x 10 + 0.2 x 39.4 = 15.9 percent. Then 20.6, 24.3 and so on. This is why the CheapSolar lab shows a small change in 2030 and a larger one by 2050. GCAM tracks each plant's vintage, so this slow turnover is built in.

## Slide 13: Where future cost assumptions come from: learning curves
SIDE BY SIDE
Installed capacity | Cost index (20% learning rate)
1× today | 100
2× today | 80
4× today | 64
8× today | 51
16× today | 41
Each doubling of capacity cuts cost by 20%. Illustrative learning rate.
Notes: Analysts often build future cost paths from learning curves: every doubling of total installed capacity cuts cost by a fixed percentage. In the GCAM releases we use, costs are read from input files by year rather than learned inside the model during a run, so a learning curve is one way to write those input numbers. The GCAM v8.2 Technology Representation page describes costs as levelised input costs and does not mention learning inside the model; still check your release before teaching.

## Slide 14: How to build a CheapSolar scenario
KEY IDEA
1
Copy the configuration
cp configuration_​ref.xml config_​cheapsolar.​xml. Never edit the original.
2
Add one file, last
List solar_adv.xml at the end of the inputs, just before the solver line. Later files win.
3
Rename the scenario
Change scenarioName from Reference to CheapSolar, or your results overwrite each other's labels.
4
Compare, don't eyeball
Subtract Reference from CheapSolar year by year in R.
Notes: solar_adv.xml ships with GCAM and holds lower solar costs, so nobody writes XML by hand today. If a student forgets to change the scenario name, the run is stored as a second Reference with a later date; this is a useful mistake to discuss. Confirm before the lab that solar_adv.xml exists in your release.

## Slide 15: Common mix-ups
WATCH OUT
Not quite
Better
GCAM shows that solar will get cheaper
You told it so. Future costs are inputs; cheap solar winning partly restates your assumption.
Comparing two scenarios' totals by eye
Always compute the difference from Reference, year by year.
A cheaper technology takes over within one period
Only new investment shifts. Old plants keep running until they retire.
Notes: These three cover most worksheet 7 errors. The second becomes a habit for the rest of the course: every result is reported as a difference from Reference.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Levelised cost The average cost of one unit of output (for example one MWh) over a plant's whole life, including building, fuel and any carbon price.
Efficiency How much useful output you get per unit of fuel. A 50% efficient plant burns 2 MWh of gas for every 1 MWh of electricity.
Vintage The year a plant was built. GCAM keeps track of vintages, so old plants keep running until they retire.
Add-on file An extra input file listed last in the configuration. It overrides earlier data, so you can change one assumption without editing the originals.
Learning rate The percentage a technology's cost falls each time its total installed capacity doubles. A common way to build future cost assumptions.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 8: CheapSolar versus Reference
HANDS-ON LAB
Build and start a CheapSolar run with an add-on file, then add the instructor's CheapSolar results to your project and compute differences from Reference.
Script: labs/lab8.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Build and start a CheapSolar run with an add-on file, then add the instructor's CheapSolar results to your project and compute differences from Reference. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Build the CheapSolar run (Terminal tab)
LAB · STEP 1 OF 4
Copy the configuration, make the two edits shown in the snippet file, and start the run.
cd ~/gcam/exe
tail -n 3 logs/main_log.txt # did lab 7 finish?
cp configuration_ref.xml config_cheapsolar.xml
# edit config_cheapsolar.xml (two changes), then:
nohup ./gcam.exe -C config_cheapsolar.xml &
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: The two edits are in gcam-files/lab8_cheapsolar_config_snippet.xml: add solar_adv.xml as the last input before the solver line, and change scenarioName to CheapSolar. Students can edit the file in the RStudio editor. This is the last lab with a complete script.

## Slide 19: Add CheapSolar to your project
LAB · STEP 2 OF 4
Load last week's project and add the new scenario. Queries already stored for Reference are not run again.
library(tidyverse)
library(rgcam)
db_dir <- "/course/gcam/output" # from instructor
conn <- localDBConn(db_dir, "database_basexdb")
prj <- loadProject("output/gcam_course.dat")
prj <- addScenario(conn, prj, "CheapSolar",
"gcam-files/course_queries.xml")
elec <- getQuery(prj, "elec gen by subsector") |>
filter(region == "Japan") # your region
Notes: getQuery now returns both scenarios stacked, with the scenario column telling them apart. Replace db_dir with the real server path.

## Slide 20: Take differences from Reference
LAB · STEP 3 OF 4
Make a small Reference table, join it to CheapSolar by fuel and year, and subtract.
ref <- elec |>
filter(scenario == "Reference") |>
select(subsector, year, ref = value)
dif <- elec |>
filter(scenario == "CheapSolar") |>
left_join(ref, by = c("subsector", "year")) |>
mutate(change = value - ref)
ggplot(dif, aes(year, change, fill = subsector)) +
geom_col()
Notes: If left_join warns about a many-to-many match, the query returned more than one row per fuel group and year; the script has two commented lines that add them up first. Expected: change is zero in historical years, because the add-on changes future costs only.

## Slide 21: Let rchart draw the standard charts
LAB · STEP 4 OF 4
rchart wants columns scenario, region, year, value, class and param. With scenRef set, it also draws difference charts.
library(rchart)
rc <- elec |>
select(scenario, region, year, value,
class = subsector) |>
mutate(param = "Electricity")
charts <- chart(rc, scenRef = "Reference",
save = FALSE)
names(charts)
charts$chart_class_diff_absolute
Notes: Print names(charts) first, because names gain a region suffix when the table holds more than one region. The teaching point: the rchart difference chart and the hand-made one show the same numbers.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
dif has one row per fuel group and year
Changes are zero before the first future period
Solar's change is positive; coal and gas lose a little each
Worksheet questions
1
By how many units does solar generation change in your region in 2030 and in 2050? Why is 2050 larger?
2
Does total electricity change? Explain using the electricity price.
3
Repeat the difference for CO2 emissions. Is cheap solar alone a climate policy?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
Energy flows from resources through transformation to final demand; each handover is a market
2
Levelised cost = non-energy cost + fuel ÷ efficiency + carbon price × emissions
3
Future costs are assumptions you set; learning curves are one way to choose them
4
A cost cut shifts new investment fast, but the fleet turns over slowly
5
Always report results as differences from Reference
Next: week 9
Week 9 turns to the other half of GCAM: farms, forests and water, and how energy, land and water pull on each other.
Practise
Interactive course, week 8: try the learning explorer and the 5-question quiz.
Readings: rchart package guide; GCAM v8.2 documentation: Energy Supply, Energy Demand, Technology Representation
Notes: Go back to the goals from the start: Trace energy from resources through power plants and refineries to final demand; Calculate a technology's levelised cost from its three parts; Explain why new investment changes fast but the whole fleet changes slowly; Run a scenario with an add-on file and compute differences from Reference in R. Ask students to rate themselves on each. Then point to next week: Week 9 turns to the other half of GCAM: farms, forests and water, and how energy, land and water pull on each other.