## Slide 1: Land, water and bioenergy
WEEK 9 OF 15 · STAGE 2: GCAM IN DEPTH
Why a climate policy ends up on the farm
New R skill rmap for maps; first look inside gcamdata: how R turns source data into GCAM input files
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 9: Land, water and bioenergy. Why a climate policy ends up on the farm. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: rmap for maps; first look inside gcamdata: how R turns source data into GCAM input files.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 9 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Calculate profit per hectare and land shares for competing uses
2
Estimate the land needed for a given amount of bioenergy
3
Explain why water is balanced by river basin, not by region
4
Draw maps of GCAM results with rmap and find where an input file comes from in gcamdata
Big question If we grow crops for energy, where does the land and water come from, and what gives way?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: If we grow crops for energy, where does the land and water come from, and what gives way?

## Slide 4: A carbon price reaches the countryside
LET'S START WITH A QUESTION
Put a price on carbon for power plants. Soon farmland gets more valuable, forests may grow, and some rivers start to run short.
How can a policy aimed at power stations change what farmers plant?
Notes: Let students suggest the chain before you show it. Someone usually gets to bioenergy. The whole lecture is about following that chain: energy, land and water linked together, which is the energy-water-land nexus.

## Slide 5: Land is rented to the highest bidders
AN EVERYDAY PICTURE
Imagine every patch of land is a flat for rent. A wheat farmer, a forester and an energy-crop grower all bid. Each can pay up to what the land earns them. The best payers win more flats, but never all of them, because soils, climates and habits differ.
What it means for models
1
The bid is profit per hectare
2
Higher profit wins more land, gradually
3
Protected land is not for rent
Notes: This is the week 7 logit rule with profit in place of cost. More profit is better, so the exponent is positive. This image is stop three of the study guide memory route, the greenhouse.

## Slide 6: Worked example: wheat or energy grass?
WORKED EXAMPLE · STEP BY STEP
Problem Profit per hectare = (price − cost) × yield. Wheat: $200/t, cost $120/t, 3 t/ha. Grass: $60/t, cost $30/t, 10 t/ha.
1
Wheat: (200 − 120) × 3 = 80 × 3 = $240 per ha
2
Grass: (60 − 30) × 10 = 30 × 10 = $300 per ha
3
Share by profit, exponent 1: total = 240 + 300 = 540
4
Wheat: 240 ÷ 540 = 44%; grass: 300 ÷ 540 = 56%
Answer
Wheat 44%, energy grass 56% of the contested land
Notes: Numbers are illustrative, from the study guide. Note that grass wins on profit even though wheat earns more per tonne, because grass yields more tonnes per hectare. GCAM shares land with the relative-cost logit on profit, with a positive exponent, inside a nest of land types (Source: GCAM v8.2 documentation, Economic Choice and Land pages). Real exponents differ by nest; the simple rule here shows the idea.

## Slide 7: A stronger exponent moves more land to the winner
PICTURE THE NUMBERS
Chart: Logit exponent on profit
| Exponent 1 | Exponent 3
Wheat ($240/ha) | 44.4 | 33.9
Energy grass ($300/ha) | 55.6 | 66.1
Illustrative, computed from the share rule
Read it like this
1
Exponent 3: 240³ = 13.8 million, 300³ = 27.0 million
2
Shares 34% and 66%
3
A carbon price raises grass profit, so it gains more
Notes: Same idea as the week 7 chart: the exponent sets how sharply shares react to a profit gap. A carbon price raises the bioenergy price, which raises the grass profit and pulls still more land toward it.

## Slide 8: Quick check
QUICK CHECK · THINK, THEN VOTE
Maize: $180/t, cost $100/t, yield 4 t/ha. Grass earns $300/ha. With exponent 1, what share goes to maize?
A
About 37%
B
About 48%
C
About 52%
D
About 60%
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: about 52 percent. Maize profit = (180 - 100) x 4 = 320 per hectare. Share = 320 / (320 + 300) = 320 / 620 = 51.6 percent. This is the study guide's try-it question for week 9.

## Slide 9: Quick check: answer
QUICK CHECK · ANSWER
Maize: $180/t, cost $100/t, yield 4 t/ha. Grass earns $300/ha. With exponent 1, what share goes to maize?
A
About 37%
B
About 48%
C
About 52%
D
About 60%
Notes: Answer: about 52 percent. Maize profit = (180 - 100) x 4 = 320 per hectare. Share = 320 / (320 + 300) = 320 / 620 = 51.6 percent. This is the study guide's try-it question for week 9.

## Slide 10: Land is shared in nested rounds
HOW IT WORKS
1
All land
Protected land is set aside first and stays put
2
Big uses
Cropland, forest, pasture and shrubland compete
3
Crops
Wheat, maize, rice, energy crops and more compete
4
Water use
Each crop splits into irrigated and rainfed
Land is solved in more than 300 land subregions. Energy crops appear only in future periods.
Notes: The sharing is nested, so crops compete with each other first and cropland then competes with forest and pasture. The irrigated and rainfed split, plus high and low fertiliser, is where water and inputs enter the land system (Source: GCAM v8.2 documentation, Land page). Dedicated energy crops are absent from historical data and enter in future periods; the documentation does not state this directly, so check it before teaching.

## Slide 11: Worked example: land for 10 EJ of bioenergy
WORKED EXAMPLE · STEP BY STEP
Problem How much land does 10 EJ a year of energy grass need? Yield 10 t/ha; energy content 18 GJ per tonne.
1
Energy per hectare: 10 t × 18 GJ = 180 GJ per ha
2
10 EJ = 10 × 10^9 GJ
3
Land = 10 × 10^9 ÷ 180 = 55.6 million ha
4
Halve the yield to 5 t/ha: land doubles to 111 million ha
Answer
About 56 million hectares at 10 t/ha, twice that at 5 t/ha
Notes: Illustrative yield and energy content. The lesson is that bioenergy land scales directly with ambition and inversely with yield. Large mitigation scenarios can ask for tens of exajoules, so land becomes a real constraint. The widget lets students try other yields and amounts.

## Slide 12: Each river basin has a staircase of water supply
SIDE BY SIDE
Source | Cost ($ per m³) | Available
Renewable water (runoff) | 0.05 | first 100 units
Groundwater (finite stock) | 0.20 | next 15 units
Desalination | 1.00 | anything beyond 115
Demand 110 → price $0.20. Demand 125 → price $1.00. Illustrative numbers.
Notes: Water is the third kind of market after energy and land, and it clears by basin: the basin's water price is adjusted until demand fits the available supply. Cheap renewable water comes first, then costlier groundwater and desalination, so a modest rise in demand can trigger a big price jump. Six kinds of demand draw on it: agriculture, livestock, electricity generation, primary energy, manufacturing and municipal (Source: GCAM v8.2 documentation, Water Supply and Water Demand pages).

## Slide 13: Why the map matters for water
COMPARE
Region view
One number for the whole region
Can look comfortable on average
Hides where the stress is
Basin view
One market per river basin
A basin can cross borders
Shows the one dry basin carrying most withdrawals
Notes: A region can contain several basins and a basin can span several regions. That is why the lab maps water on the basin map and energy on the region map. The study guide's trap: a region total can look fine while one basin inside it is stressed.

## Slide 14: The nexus: follow one carbon price
KEY IDEA
1
Energy → land
A carbon price raises demand for bioenergy, so energy crops become more profitable.
2
Land shifts
Energy crops take land from food, pasture or forest, and crop prices rise.
3
Land → water
More irrigated crops raise withdrawals in some basins and push water prices up.
4
Water → energy
Power plants need cooling water, and fertiliser and farm fuel need energy.
Notes: This slide is why the model is called integrated: GCAM solves all three systems together. Walk the cards in order with one example region. In the lab, the maps show where these pressures land.

## Slide 15: Common mix-ups
WATCH OUT
Not quite
Better
The region has plenty of water, so no water problem
Water clears by basin. One basin inside the region can be badly stressed.
Bioenergy is free carbon removal
It uses land that could grow food or forest, plus water and fertiliser.
The most profitable crop takes all the land
Land shares follow a logit rule, so shares shift gradually.
Notes: The first two are the study guide's traps and come up on quiz 2. The third repeats the week 7 lesson for land.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Yield How much a crop produces per unit of land, for example 3 tonnes of wheat per hectare.
Profit per hectare (Price − cost) × yield. The amount a land use earns on one hectare; GCAM shares land using it.
River basin The area drained by one river system. GCAM balances water supply and demand basin by basin.
Water withdrawal Water taken from a river, lake or aquifer. Part is returned; the part not returned is called consumption.
Nexus The links between energy, water and land: a change in one system moves the other two.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 9: maps and a first look in gcamdata
HANDS-ON LAB
Map cropland by region and water withdrawals by basin with rmap, then open gcamdata and find which file holds solar's capacity factor.
Script: labs/lab9.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Map cropland by region and water withdrawals by basin with rmap, then open gcamdata and find which file holds solar's capacity factor. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Map cropland by region
LAB · STEP 1 OF 4
Add up cropland per region in 2050, then match GCAM's region names to the map's names.
prj <- loadProject("output/gcam_course.dat")
crops <- prj |>
getQuery("aggregated land allocation") |>
filter(scenario == "Reference", year == 2050,
landleaf == "crops") |>
group_by(region) |>
summarise(value = sum(value)) |>
mutate(subRegion =
str_replace_all(region, "-", "_"))
rmap::map(crops, shape = rmap::mapGCAMReg32,
save = FALSE)
Notes: Write rmap::map in full every time, because purrr also has a map function. str_replace_all swaps the hyphen in EU-12 and EU-15 for an underscore so the names match. rmap warns if any region fails to match. From this week scripts have gaps; solutions/lab9_solution.R is for the instructor. Since GCAM 8.1 Ukraine is its own region in place of the old Europe_Eastern; if rmap's 32-region map predates that, Ukraine shows as unmatched, so check before the lab.

## Slide 19: Map water by river basin (gap 1)
LAB · STEP 2 OF 4
Turn GCAM's water resource names into basin names, then draw them on rmap's basin map. Fill the gap with the basin map's name.
basin <- prj |>
getQuery("water withdrawals by basin") |>
filter(scenario == "Reference", year == 2050) |>
mutate(subRegion = str_remove(
basin, "_water withdrawals")) |>
group_by(subRegion) |>
summarise(value = sum(value)) |>
left_join(rmap::mapping_gcambasins,
by = "subRegion") |>
select(subRegion = subRegionMap, value)
rmap::map(basin, shape = rmap::___, # basin map
save = FALSE)
Notes: The answer is mapGCAMBasins; typing rmap::mapGCAM and pressing Tab shows the candidates. If the column is not called basin on your server, names() on the query result shows what it is called. Expected: a world map cut into river basins, most pale and a few dark.

## Slide 20: Open gcamdata (read only)
LAB · STEP 3 OF 4
gcamdata is the R package that builds every GCAM input file. It is a chain of chunks; each lists what it reads and writes.
gcamdata_dir <- path.expand("~/gcamdata")
devtools::load_all(gcamdata_dir)
chunks <- find_chunks()
count(chunks, module)
inputs_of("module_energy_L223.electricity")
outputs_of(
"module_energy_elec_tech_scenarios_xml")
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: outputs_of for the tech scenarios chunk lists solar_adv.xml from week 8 beside matching wind and nuclear files. Each student needs a personal gcamdata copy. Nothing is edited today; that comes in lab 10.

## Slide 21: Find solar's capacity factor (gap 2)
LAB · STEP 4 OF 4
Read one assumption file. Lines starting with # are comments. Fill the gap with the subsector that holds the PV technology.
cf <- read_csv(file.path(gcamdata_dir,
"inst/extdata/energy",
"A23.globaltech_capacity_factor.csv"),
comment = "#")
filter(cf, subsector == "___") # holds PV
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: The answer is solar. Close by naming the chain aloud: a number in a CSV file, a chunk, an XML file, a GCAM run. Lab 10 changes the first link.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
A world map in 32 pieces with no unmatched-region warning
A basin map where a few basins stand out dark
filter(cf, ...) shows the PV row with values by year
Worksheet questions
1
Which three regions have the most cropland in 2050 under Reference?
2
Pick a basin that is dark on your map. Why might a region total hide its stress?
3
Which CSV file holds solar's capacity factor, and which chunk reads it?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
Land goes to uses with higher profit per hectare, shared gradually by a logit rule
2
Bioenergy land = energy wanted ÷ (yield × energy per tonne); low yields need much more land
3
Water markets clear by river basin, priced by the most expensive source needed
4
Energy, land and water are solved together: the nexus
Next: week 10
Week 10 adds emissions and policy: carbon prices, net-zero limits and carbon removal, and your first change inside gcamdata.
Practise
Interactive course, week 9: try the land explorer and the 5-question quiz.
Readings: rmap package guide; gcamdata overview; GCAM v8.2 documentation: Land, Water Supply, Water Demand, GCAM Data System
Notes: Go back to the goals from the start: Calculate profit per hectare and land shares for competing uses; Estimate the land needed for a given amount of bioenergy; Explain why water is balanced by river basin, not by region; Draw maps of GCAM results with rmap and find where an input file comes from in gcamdata. Ask students to rate themselves on each. Then point to next week: Week 10 adds emissions and policy: carbon prices, net-zero limits and carbon removal, and your first change inside gcamdata.