## Slide 1: Emissions, carbon removal and policy
WEEK 10 OF 15 · STAGE 2: GCAM IN DEPTH
Set a price or set a limit: two doors to the same room
New R skill gcamdata: finding a chunk, editing an assumption, running the driver
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 10: Emissions, carbon removal and policy. Set a price or set a limit: two doors to the same room. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: gcamdata: finding a chunk, editing an assumption, running the driver.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 10 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Trace how GCAM turns activity into emissions and Hector turns emissions into warming
2
Explain the mirror between a carbon price and an emissions limit
3
Describe three ways GCAM removes CO2 and what each one costs the rest of the model
4
Run policy scenarios and change one assumption in gcamdata
Big question Should a government say 'emissions cost $50 a tonne' or 'emissions must reach zero by 2050', and what does a model do with each?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: Should a government say 'emissions cost $50 a tonne' or 'emissions must reach zero by 2050', and what does a model do with each?

## Slide 4: Two ways to tell a model about climate policy
LET'S START WITH A QUESTION
Option A: 'Every tonne of CO2 costs $50.' Option B: 'Emissions must be zero in 2050.'
With option A, what does the model work out? With option B?
Notes: Give pairs one minute. The answer: with a price the model finds emissions; with a limit it finds the price. That mirror is the core of this week and you met it in week 4 with prices against quantities.

## Slide 5: From activity to temperature
HOW IT WORKS
1
Activity
Fuel burned, land cleared, goods made, animals raised
2
Emissions
Activity × emission factor, less any abatement
3
Hector
Turns emissions into concentrations and forcing
4
Temperature
Global mean warming for the scenario
Steps 1 and 2 happen inside GCAM; steps 3 and 4 are Hector, the model you ran in week 2
Notes: At every time step GCAM passes its emissions to Hector, which returns concentrations, forcing and temperature (Source: GCAM v8.2 documentation, Climate page). Fossil CO2 comes from fuel use and carbon content; land-use change CO2 is tracked in the land system. A good check question: which steps change if you swap Hector for another climate model? Answer: 3 and 4 only.

## Slide 6: Worked example: counting emissions
WORKED EXAMPLE · STEP BY STEP
Problem Emissions = activity × emission factor × (1 − abatement share). A region makes 1,000 TWh of coal power; a landfill emits 2 Mt of methane.
1
Coal power factor: 0.9 Mt CO2 per TWh (0.9 t per MWh)
2
CO2 = 1,000 × 0.9 = 900 Mt
3
A carbon price makes 30% methane capture worthwhile (cost curve)
4
Methane = 2 × (1 − 0.30) = 2 × 0.7 = 1.4 Mt
Answer
900 Mt CO2 from power; methane falls from 2 to 1.4 Mt
Notes: Illustrative numbers from the study guide. A carbon price cuts CO2 mainly by changing which technologies are used, and cuts other gases by abatement along cost curves read from input files. The 0.9 factor is week 4's coal number.

## Slide 7: A toll road or a gate
AN EVERYDAY PICTURE
A toll road charges every car $5. You know the cost per car, but not how many will drive. A gate lets exactly 500 cars through. You know the number, but drivers bid up what a pass is worth. A carbon price is the toll; an emissions limit is the gate.
What it means for models
1
Price fixed → quantity (emissions) found
2
Cap fixed → price found
3
Same cost curve, read in opposite directions
Notes: This makes the mirror concrete. In GCAM's CarbonPrice scenario you set the toll and read emissions. In NetZero you set the gate and GCAM searches for the price, which is why NetZero takes longer to solve.

## Slide 8: The course's carbon price rises 5% a year
PICTURE THE NUMBERS
Chart: Year
| 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055 | 2060 | 2065 | 2070 | 2075 | 2080 | 2085 | 2090 | 2095 | 2100
Carbon price (1990 $ per tonne of carbon) | 25 | 31.9 | 40.7 | 52 | 66.3 | 84.7 | 108 | 137.9 | 176 | 224.6 | 286.7 | 365.9 | 467 | 596 | 760.7 | 970.8
From carbon_​price_global.​xml used in lab 10, copied from GCAM's carbon_​tax_25_5.xml
Read it like this
1
Starts at 25 in 2025, × 1.05 each year
2
2050: 25 × 1.05^25 ≈ 85
3
Per tonne of CO2, divide by 3.67
Notes: A price that rises at a steady percentage is common in modelling because it treats a tonne cut later as worth the same, after discounting, as a tonne cut now; economists link this to Hotelling's rule. Stress the units: GCAM prices are in 1990 dollars per tonne of carbon, so 85 per tonne of carbon is about 23 per tonne of CO2. The units are confirmed by the GCAM v8.2 documentation's policy examples, which state prices in 1990 dollars per tonne of carbon.

## Slide 9: Quick check
QUICK CHECK · THINK, THEN VOTE
A carbon price starts at 25 and rises 5% a year. Roughly what is it 10 years later?
A
30
B
35
C
41
D
50
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: about 41. 1.05 to the power 10 is 1.63, and 25 x 1.63 = 40.7. A common wrong answer is 37.5, from adding 5 percent of 25 ten times; growth compounds.

## Slide 10: Quick check: answer
QUICK CHECK · ANSWER
A carbon price starts at 25 and rises 5% a year. Roughly what is it 10 years later?
A
30
B
35
C
41
D
50
Notes: Answer: about 41. 1.05 to the power 10 is 1.63, and 25 x 1.63 = 40.7. A common wrong answer is 37.5, from adding 5 percent of 25 ten times; growth compounds.

## Slide 11: Policy enters as a price, a limit or a rule
SIDE BY SIDE
Policy type | You set | GCAM finds | Course scenario
Carbon price | A price each period | Emissions each period | CarbonPrice
Emissions limit | A cap each period | The price that meets it | NetZero
Climate target | A forcing level in a year | A least-cost price path | Not run: slow
Sector or land rule | A share, cap or protected land | The tax or subsidy needed | Not run
Regions that share a market name share one carbon price
Notes: Rows one and two are mirror images: set a price and GCAM finds emissions, or set a limit and the solver finds the price that meets it. The documentation's Policies page lists carbon or greenhouse gas prices, emissions constraints and climate constraints, plus standards for sectors and land. It has no net-zero or NDC page, so our NetZero scenario is built as an emissions constraint, and a pledge like an NDC must be translated into caps or prices by the modeller; students state that choice in the project report.

## Slide 12: Worked example: price or cap, the mirror
WORKED EXAMPLE · STEP BY STEP
Problem Suppose each extra 1% cut costs $2 more per tonne, so price = 2 × cut%. A straight-line cost curve, for illustration.
1
CarbonPrice: you set $50
2
GCAM finds the cut: 50 ÷ 2 = 25% below Reference
3
NetZero-style cap: you require a 60% cut
4
GCAM finds the price: 2 × 60 = $120 per tonne
Answer
Price $50 → 25% cut; cap of 60% cut → price $120
Notes: Same curve read in opposite directions. Real cost curves bend upward, so the last cuts are much dearer than the first. The widget lets students set a price path and see the cut each year using this curve.

## Slide 13: Three ways GCAM removes CO2
KEY IDEA
1
Bioenergy with capture
Grow crops, burn them for energy, store the CO2. Needs land, water and fertiliser (week 9).
2
More forest
Trees store carbon as they grow. Needs land, and uptake takes 30 to 100 years.
3
Direct air capture
Machines pull CO2 from the air. Needs a lot of electricity or heat.
Notes: Each option sits in a part of the model students already know, so each has a visible cost. The Land page's 30 to 100 years for forests to take up their carbon matters for 2050 targets. Carbon in land is valued as a subsidy to landowners for holding carbon stocks, tied to the carbon price (Source: GCAM v8.2 documentation, Land and Policies pages).

## Slide 14: Balancing a net-zero year
NUMBERS TO REMEMBER
10 Gt
CO2 still emitted in 2050, to be balanced by removals
3 Gt
of that removed by direct air capture
18 EJ
energy needed: 3 × 10^9 t × 6 GJ per tonne
Illustrative split: 4 Gt bioenergy with capture + 3 Gt forest + 3 Gt air capture = 10 Gt
Notes: Work the arithmetic: 3 billion tonnes times 6 GJ per tonne is 18 billion GJ, or 18 EJ. That energy must itself come from somewhere, ideally low-carbon. The 6 GJ per tonne is a round illustrative number; published estimates vary widely, so check before quoting it.

## Slide 15: Common mix-ups
WATCH OUT
Not quite
Better
Net zero means no emissions
It means remaining emissions equal removals, and every removal uses land, energy or water.
GCAM has a built-in setting for each country's NDC
Turning a pledge into caps or prices is your modelling choice. State it in your report.
GCAM carbon prices are per tonne of CO2
They are in 1990 dollars per tonne of carbon. Divide by 3.67 for CO2.
Notes: The first two are the study guide traps. The third catches many students when they compare GCAM prices with news reports, which quote dollars per tonne of CO2 in today's money.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Abatement Cutting emissions of a gas, for example capturing methane at a landfill. GCAM reads its cost from cost curves.
Emissions limit A cap on how much may be emitted each period. The model finds the carbon price needed to meet it.
Carbon dioxide removal Taking CO2 out of the air and storing it, for example in forests, or with bioenergy plus capture, or machines (CDR).
Net zero Remaining emissions equal removals, so the total added to the air is zero. It does not mean no emissions.
NDC Nationally Determined Contribution: a country's climate pledge under the Paris Agreement.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 10: CarbonPrice, NetZero and gcamdata
HANDS-ON LAB
Start a CarbonPrice run, compare CarbonPrice and NetZero with Reference for emissions, temperature and price, then change one number in gcamdata and rebuild.
Script: labs/lab10.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Start a CarbonPrice run, compare CarbonPrice and NetZero with Reference for emissions, temperature and price, then change one number in gcamdata and rebuild. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Build the CarbonPrice run (Terminal tab)
LAB · STEP 1 OF 4
Same routine as week 8: copy, make two edits, start. The add-on file is carbon_​price_global.​xml from your gcam-files folder.
cd ~/gcam/exe
cp configuration_ref.xml config_carbonprice.xml
# edit config_carbonprice.xml (two changes), then:
nohup ./gcam.exe -C config_carbonprice.xml &
tail -n 3 logs/main_log.txt
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: The edits are in gcam-files/lab10_carbonprice_config_snippet.xml: add carbon_price_global.xml as the last input with its full path, and set scenarioName to CarbonPrice. NetZero uses two policy files that ship with GCAM and was run by the instructor ahead of time because a limit makes GCAM search for the price.

## Slide 19: Add both policy scenarios (gap 1)
LAB · STEP 2 OF 4
A for loop adds each scenario. Fill the gap with the second policy scenario's name.
prj <- loadProject("output/gcam_course.dat")
for (s in c("CarbonPrice", "___")) { # 2nd policy
prj <- addScenario(conn, prj, s,
"gcam-files/course_queries.xml")
}
co2 <- getQuery(prj, "CO2 emissions by region") |>
group_by(scenario, year) |>
summarise(value = sum(value), .groups = "drop")
ggplot(co2, aes(year, value, colour = scenario)) +
geom_line()
Notes: The answer is NetZero; listScenariosInDB(conn) shows the exact name. conn is created as in lab 8 at the top of the script. The full version is solutions/lab10_solution.R. The NetZero limit covers all greenhouse gases, so its CO2 line can end slightly above or below zero.

## Slide 20: Temperature and carbon prices (gap 2)
LAB · STEP 3 OF 4
Fill the gap with the query title that returns global mean temperature. Then look at the carbon price in each market.
temp <- getQuery(prj, "___") # a query title
ggplot(temp, aes(year, value, colour = scenario)) +
geom_line()
price <- getQuery(prj, "CO2 prices")
ggplot(price, aes(year, value, colour = scenario)) +
geom_line() +
facet_wrap(~ market)
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: The answer is the global mean temperature query; listQueries(prj) shows its exact title. Temperature comes from Hector, which students ran alone in lab 2. CO2 prices is empty for Reference and CheapSolar and rgcam warns; that is correct.

## Slide 21: Change one number in gcamdata (gap 3)
LAB · STEP 4 OF 4
In your gcamdata project, raise solar's 2050 capacity factor in one CSV, rebuild only what depends on it, and compare.
devtools::load_all(".")
obj <- "L223.GlobalIntTechCapFac_elec"
before <- drake::readd(obj, character_only = TRUE)
file.edit(file.path("inst/extdata/energy",
"A23.globaltech_capacity_factor.csv"))
# change the PV value for 2050, save, then:
devtools::load_all(".")
driver_drake()
after <- drake::readd(obj, character_only = TRUE)
filter(after, subsector.name == "solar",
year == ___) # the year you edited
Notes: The answer is 2050. The capacity factor is the share of the year a plant runs at full output; a higher value makes solar cheaper per MWh. driver_drake rebuilds only chunks downstream of the edited file. Warn students not to touch R/constants.R, which forces a full rebuild.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
Three or four emission lines, with NetZero falling to about zero by 2050
Temperature lines stay close until mid-century, then separate
after shows your new 2050 capacity factor for solar
Worksheet questions
1
By how much are 2050 CO2 emissions below Reference in CarbonPrice and in NetZero?
2
Why do the temperature lines separate later than the emission lines? Use week 2's idea of cumulative emissions.
3
List the files driver_​drake rebuilt after your edit. Which XML file would GCAM read?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
GCAM counts emissions from activity; Hector turns them into warming
2
A carbon price fixes cost and finds emissions; a limit fixes emissions and finds the price
3
The course price starts at 25 (1990 $/tC) in 2025 and rises 5% a year
4
Net zero balances leftover emissions with removals, which use land, energy or water
5
Turning pledges into model inputs is a choice you must state
Next: week 11
Week 11 opens the advanced stage: optimisation models that look ahead, starting with a three-technology power system as a linear program.
Practise
Interactive course, week 10: try the carbonprice explorer and the 5-question quiz.
Readings: Fawcett et al. (2015), Can Paris pledges avert severe climate change?, Science; gcamdata guide: running the driver; GCAM v8.2 documentation: Emissions, Climate (Hector), Policies and costs, Policy examples
Notes: Go back to the goals from the start: Trace how GCAM turns activity into emissions and Hector turns emissions into warming; Explain the mirror between a carbon price and an emissions limit; Describe three ways GCAM removes CO2 and what each one costs the rest of the model; Run policy scenarios and change one assumption in gcamdata. Ask students to rate themselves on each. Then point to next week: Week 11 opens the advanced stage: optimisation models that look ahead, starting with a three-technology power system as a linear program.