## Slide 1: Optimisation models
WEEK 11 OF 15 · STAGE 3: ADVANCED METHODS
One goal, many limits: how planners' models choose
New R skill lpSolve: objective, constraints, reading shadow prices
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 11: Optimisation models. One goal, many limits: how planners' models choose. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: lpSolve: objective, constraints, reading shadow prices.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 11 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Write a small energy problem as an objective and constraints
2
Solve a three-technology power system by hand and with lpSolve
3
Read a shadow price and explain why it acts like a carbon price
4
Contrast GCAM's simulation with optimisation and CGE models
Big question If one planner could choose the whole power mix with perfect knowledge, what would they build, and what would a climate cap cost?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: If one planner could choose the whole power mix with perfect knowledge, what would they build, and what would a climate cap cost?

## Slide 4: You are the planner
LET'S START WITH A QUESTION
Supply 100 TWh of electricity at the lowest cost, using coal, gas and solar, while emitting no more than 40 Mt of CO2.
Would you use all the solar you are allowed?
Notes: Let pairs try for two minutes with the table on the next slide. Most will fill solar to its limit of 30. The surprise of the lecture is that the cheapest plan uses only 27.8 TWh of solar. Keep the guesses on the board and return to them after the worked example.

## Slide 5: An optimisation model is a sat-nav for an energy system
AN EVERYDAY PICTURE
You give a sat-nav one goal, the fastest route, and the limits: roads, one-way streets, a closed bridge. It searches and returns the single best route. An optimisation model does the same with cost as the goal and demand, plant sizes and emission caps as the limits.
What it means for models
1
Goal = objective (lowest total cost)
2
Limits = constraints (demand, capacity, cap)
3
Answer = one best plan, not a range
Notes: Introduce the words objective and constraint only after the picture. Stress that the answer is one plan. That is very different from GCAM, which spreads market shares across options by cost, as students saw in week 7.

## Slide 6: The toy power system from lab 11
SIDE BY SIDE
Technology | Cost $/MWh | tCO2 per MWh | Limit TWh
Coal | 60 | 0.9 | 60
Gas | 70 | 0.4 | 50
Solar | 80 | 0 | 30
Demand |  |  | 100 in total
Same costs and emission factors as the week 4 market. Illustrative numbers, not a real country.
Notes: Point out that the costs and emission factors are the week 4 numbers, so students already know that a carbon price of 20 makes gas beat coal and 25 makes solar beat gas. The limits are new: each plant can only produce so much. Write the objective on the board: 60 times coal plus 70 times gas plus 80 times solar. It is only a weighted sum, which is what makes it linear.

## Slide 7: Worked example: no cap, fill the cheapest first
WORKED EXAMPLE · STEP BY STEP
Problem Meet 100 TWh at the lowest cost with no emissions cap.
1
Coal is cheapest: use its full limit, 60 TWh
2
Still need 100 − 60 = 40 TWh: take it from gas, the next cheapest
3
Cost = 60 × 60 + 40 × 70 = 3,600 + 2,800 = $6,400 million
4
Emissions = 0.9 × 60 + 0.4 × 40 = 54 + 16 = 70 Mt
Answer
Coal 60, gas 40, solar 0 TWh; $6,400 million; 70 Mt CO2
Notes: Filling the cheapest plant first is called the merit order. Units: dollars per MWh times TWh gives million dollars, and tonnes per MWh times TWh gives million tonnes. In the lab, lpSolve should return exactly these numbers for part A.

## Slide 8: Worked example: add a 40 Mt cap
WORKED EXAMPLE · STEP BY STEP
Problem Same system, but emissions must be 40 Mt or less. Find the cheapest mix.
1
Swapping coal for gas costs 10 $/MWh and saves 0.5 t: $20 per tonne
2
Swapping coal for solar costs 20 $/MWh and saves 0.9 t: $22.2 per tonne
3
Do the cheaper swap first: gas to its limit, 50 TWh, using 0.4 × 50 = 20 Mt
4
That leaves 40 − 20 = 20 Mt for coal: 20 ÷ 0.9 = 22.2 TWh
5
Solar fills the rest: 100 − 50 − 22.2 = 27.8 TWh
6
Cost = 22.2 × 60 + 50 × 70 + 27.8 × 80 ≈ $7,056 million
Answer Coal 22.2, gas 50, solar 27.8 TWh; about $7,056 million
Notes: The key idea is the cost per tonne avoided. Gas is the cheaper way to cut a tonne, so it is used to its limit first. Only then does solar replace coal. The exact values are 200/9, 50 and 250/9 TWh, and the cost is 7,055.6 million dollars, confirmed with a solver.

## Slide 9: The solver gives you a carbon price for free
NUMBERS TO REMEMBER
$22.2
per tonne: the shadow price of the 40 Mt cap
+$656m
extra cost of the cap: 7,056 − 6,400
38 Mt
lowest cap with any solution at all
Shadow price = (80 − 60) ÷ 0.9: the cost gap between solar and coal per tonne saved. Illustrative.
Notes: Loosen the cap by one tonne and 1 divided by 0.9 = 1.11 MWh of coal can replace solar, saving 20 x 1.11 = 22.2 dollars. Check against week 4: with a carbon price of 22.2, coal costs 60 + 0.9 x 22.2 = 80, the same as solar. So a cap and a carbon price are two views of the same result. Below 38 Mt no mix works: even solar 30, gas 50 and coal 20 emits 38 Mt.

## Slide 10: Tighter caps cost more, at a rising price per tonne
PICTURE THE NUMBERS
Chart: Emissions cap (MtCO2)
| 70 | 65 | 60 | 55 | 50 | 45 | 40
Least total cost ($ million) | 6400 | 6500 | 6611.1 | 6722.2 | 6833.3 | 6944.4 | 7055.6
Computed by solving the lab 11 system at each cap. Illustrative numbers.
Read it like this
1
70 to 65 Mt: coal swaps for gas at $20 per tonne
2
Below 65 Mt: coal swaps for solar at $22.2 per tonne
3
The slope of this line is the shadow price
Notes: Read the chart from left to right: each step tightens the cap by 5 Mt. The first step costs 100 million dollars, which is 20 dollars per tonne; every later step costs 111 million, which is 22.2 per tonne. The slope changes where the cheapest swap changes. Ask: what happens just below 38 Mt? The line simply stops, because no mix is possible.

## Slide 11: Quick check
QUICK CHECK · THINK, THEN VOTE
Why does a 37 Mt cap make lpSolve report status 2, no solution?
A
The solver ran out of time
B
Even the cleanest mix allowed emits 38 Mt
C
Solar is too expensive
D
Demand is not a constraint
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: the cleanest mix the limits allow is solar 30, gas 50 and coal 20, which emits 0.4 x 50 + 0.9 x 20 = 38 Mt. Nothing below that exists. Teach students to read status before anything else: an infeasible problem still prints numbers, and they are meaningless.

## Slide 12: Quick check: answer
QUICK CHECK · ANSWER
Why does a 37 Mt cap make lpSolve report status 2, no solution?
A
The solver ran out of time
B
Even the cleanest mix allowed emits 38 Mt
C
Solar is too expensive
D
Demand is not a constraint
Notes: Answer: the cleanest mix the limits allow is solar 30, gas 50 and coal 20, which emits 0.4 x 50 + 0.9 x 20 = 38 Mt. Nothing below that exists. Teach students to read status before anything else: an infeasible problem still prints numbers, and they are meaningless.

## Slide 13: GCAM simulates; optimisation models plan
COMPARE
Simulation: GCAM
Shares the market across options by relative cost (logit)
Decides one period at a time with no view ahead (myopic)
Asks: what might happen if a cost or policy changes?
Optimisation: MESSAGEix, REMIND, TIMES
Picks the single least-cost plan
Usually sees every period at once (perfect foresight)
Asks: what is the best plan, and what does a target cost?
Notes: Tie the left column to weeks 7 and 8, where students saw logit shares and period-by-period solving. MESSAGEix can also run in a myopic mode, so foresight is a setting, not a law. Ask: if a model knows a strict cap arrives in 2050, what does it do in 2030? It stops building coal early, which GCAM would not. Check the model descriptions against each model's documentation before teaching.

## Slide 14: How far does the model look across the economy?
KEY IDEA
1
Partial equilibrium
Balances some markets only. GCAM balances energy, land and water markets and stops at the energy bill.
2
General equilibrium (CGE)
A computable general equilibrium model follows every sector, wages, incomes and trade, so it can ask who gains and who loses.
3
The trade-off
A CGE model sees the whole economy but with little technology detail: power may be one sector with a few options.
Notes: The aim is recognition, so students know what CGE means in a paper. Tell the ripple story: a carbon price raises the cost of steel, so cars cost more, households buy fewer cars and spend elsewhere, and steel wages change. A partial equilibrium model sees only the first step. AR6 Annex III labels GCAM a partial equilibrium model; check the wording against the source before teaching.

## Slide 15: Common mix-ups
WATCH OUT
Not quite
Better
Optimisation models show what will happen
They show the cheapest plan for a planner who knows the future perfectly. Nobody does.
The shadow price is −22.2, so the cap makes money
The minus sign only says a tighter cap raises cost. Read the size, 22.2, as the carbon price.
The solver tries every possible mix
It moves along the corners of the allowed region and stops when no neighbour is cheaper.
Notes: The sign of the dual depends on the solver and on how the constraint is written, which is why the lab checks it by loosening the cap by 1 Mt and solving again. The third point matters for intuition: linear programs are fast because the best answer always sits at a corner of the allowed region.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Linear program A problem with one goal to make as small (or large) as possible and limits written as simple sums, solved by a computer.
Objective The single number the model tries to make as small as possible, here the total cost of electricity.
Constraint A rule the answer must obey, such as meeting demand, staying under a plant's limit, or staying under an emissions cap.
Shadow price How much the objective would change if one constraint were loosened by one unit. For an emissions cap it is a carbon price.
Perfect foresight The model knows every future period when it decides today. GCAM does not; it is myopic, deciding one period at a time.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 11: a power system as a linear program
HANDS-ON LAB
Write the toy power system for lpSolve, find the cheapest mix with and without a 40 Mt cap, and read the shadow prices. Then watch a MESSAGEix Westeros demonstration.
Script: labs/lab11.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Write the toy power system for lpSolve, find the cheapest mix with and without a 40 Mt cap, and read the shadow prices. Then watch a MESSAGEix Westeros demonstration. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Write the objective and constraints
LAB · STEP 1 OF 4
One cost per technology, then one row per constraint and one column per technology. Fill GAP 1 with demand.
library(lpSolve)
cost <- c(60, 70, 80) # coal, gas, solar
A <- rbind(demand = c(1, 1, 1),
coal = c(1, 0, 0),
gas = c(0, 1, 0),
solar = c(0, 0, 1))
dir <- c("=", "<=", "<=", "<=")
rhs <- c(___, 60, 50, 30) # GAP 1: demand in TWh
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: The gap is 100. lpSolve assumes every variable is zero or more, so no extra rows are needed. Ask students to predict the answer from the merit order before solving.

## Slide 19: Solve without a cap
LAB · STEP 2 OF 4
compute.​sens = TRUE asks for the shadow prices. Read status first: 0 means success.
base <- lp("min", cost, A, dir, rhs,
compute.sens = TRUE)
base$status # 0 = success, 2 = no solution
base$solution # TWh of coal, gas, solar
base$objval # total cost, million $
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: Expected: coal 60, gas 40, solar 0, total 6,400. This matches the first worked example.

## Slide 20: Add the 40 Mt cap
LAB · STEP 3 OF 4
The cap is one more row: the emission factors. Fill GAP 2 with emis and GAP 3 with 40.
emis <- c(0.9, 0.4, 0) # tCO2 per MWh
A2 <- rbind(A, co2 = ___) # GAP 2
dir2 <- c(dir, "<=")
rhs2 <- c(rhs, ___) # GAP 3: the cap
capped <- lp("min", cost, A2, dir2, rhs2,
compute.sens = TRUE)
capped$solution
sum(emis * capped$solution) # equals the cap
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: Expected: coal 22.2, gas 50, solar 27.8 and a cost of 7,055.6. Students expect solar at 30; let them find from the output why it stops at 27.8. The complete version is solutions/lab11_solution.R, released after the session.

## Slide 21: Read and check the shadow prices
LAB · STEP 4 OF 4
duals lists one number per constraint, then one per technology. Loosen the cap by 1 Mt to check the sign.
capped$duals # 5 constraints, then 3 technologies
rhs3 <- rhs2
rhs3[5] <- rhs2[5] + 1
looser <- lp("min", cost, A2, dir2, rhs3)
looser$objval - capped$objval # about -22.2
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: The full duals with the cap are 80, 0, -1.11, 0, -22.22, then 0, 0, 0. The demand dual of 80 says the next TWh must come from solar. For the last twenty minutes, run the MESSAGEix Westeros notebook as an instructor-led demonstration; students install nothing.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
Without a cap: coal 60, gas 40, solar 0; cost 6,400
With the 40 Mt cap: coal 22.2, gas 50, solar 27.8; cost about 7,056
capped$duals[5] is about −22.2, and loosening by 1 Mt saves about 22.2
Worksheet questions
1
Use the shadow price to estimate how much total cost falls if the cap is loosened from 40 to 50 Mt. Then solve it and compare.
2
Try a cap of 37 Mt. What is the status, and why?
3
Explain in two sentences why solar stops at 27.8 TWh instead of its limit of 30.
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
An optimisation model minimises one objective subject to constraints and returns one best plan
2
With a 40 Mt cap the cheapest mix is coal 22.2, gas 50, solar 27.8 TWh
3
The shadow price of the cap, $22.2 per tonne, is the carbon price that gives the same mix
4
GCAM simulates period by period; optimisers usually plan with foresight; CGE adds the whole economy
Next: week 12
Week 12 asks why different models give different answers to the same question, and places your GCAM run among other models' results.
Practise
Interactive course, week 11: try the lp explorer and the 5-question quiz.
Readings: Huppmann et al. (2019), The MESSAGEix Integrated Assessment Model and the ix modeling platform, Environmental Modelling and Software; lpSolve package documentation; GCAM v8.2 documentation: Overview (dynamic recursive), Solution and Computation
Notes: Go back to the goals from the start: Write a small energy problem as an objective and constraints; Solve a three-technology power system by hand and with lpSolve; Read a shadow price and explain why it acts like a carbon price; Contrast GCAM's simulation with optimisation and CGE models. Ask students to rate themselves on each. Then point to next week: Week 12 asks why different models give different answers to the same question, and places your GCAM run among other models' results.