## Slide 1: Why models disagree
WEEK 12 OF 15 · STAGE 3: ADVANCED METHODS
Same question, different models, different answers
New R skill Reproducible analysis: folders, sourced scripts, Git basics
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 12: Why models disagree. Same question, different models, different answers. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: Reproducible analysis: folders, sourced scripts, Git basics.

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 12 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Name the three sources of difference: structure, inputs and method
2
Explain how an intercomparison project makes model results comparable
3
Compare a GCAM run with AR6 scenarios after matching units and scope
4
Organise an analysis into sourced functions and save it with Git
Big question If several respected models get the same carbon price and give different emissions, which one should we believe, and what does the spread tell us?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: If several respected models get the same carbon price and give different emissions, which one should we believe, and what does the spread tell us?

## Slide 4: Same carbon price, three different futures
LET'S START WITH A QUESTION
Three models get the same carbon price path. By 2050 one has cut CO2 by 60%, one by 40% and one by only 30%.
Is one of them wrong, or are they telling us something?
Notes: Start with the explain-a-paper talk. Then put the question to the room. Collect answers that blame a bug, and answers that say the models assume different things. The rest of the lecture shows that disagreement is not a failure: it is the only window we have on how much the tools themselves are uncertain.

## Slide 5: Three cooks, one recipe name
AN EVERYDAY PICTURE
Ask three cooks for "a chocolate cake" and you get three cakes. One has a different oven, one used different cocoa, one followed a different method. Hand them all the same recipe card and the differences that remain point to ovens and methods.
What it means for models
1
Different oven = different model structure
2
Different cocoa = different inputs
3
Different recipe steps = different method
Notes: The shared recipe card is exactly what an intercomparison project does: it fixes the inputs it can, so the differences left over can be traced to structure and method. Keep the three words; every later slide uses them.

## Slide 6: Three reasons models give different answers
KEY IDEA
1
Structure
Which regions, sectors and technologies exist. A model with no land sector cannot trade bioenergy against food.
2
Inputs
Technology costs, resources, population, income. Your CheapSolar run changed one input and the whole mix moved.
3
Method
Simulation or optimisation, myopic or perfect foresight (week 11). The same data can give different plans.
Notes: Ask the class to sort some differences into the boxes: number of regions (structure), cost of solar in 2050 (inputs), foresight (method), base year (inputs). Inputs are the easiest to harmonise, which is why comparison projects start there. Note that Reference against CheapSolar is GCAM against GCAM, so it tests inputs and nothing else.

## Slide 7: How an intercomparison project works
HOW IT WORKS
1
Agree the task
Shared scenarios written down in a protocol
2
Each team runs it
Every model keeps its own structure and method
3
Report one way
Same variable names, same units, one template
4
Compare, explain
Where do results agree, and why not?
The AR6 files you used in lab 6 share column names because teams agreed a reporting template
Notes: A model intercomparison project is often shortened to MIP; spell it out the first time. The Stanford Energy Modeling Forum (EMF) has run many such studies. The reporting template is why data/ar6_world.csv has the same variable names for every model, which made lab 6 possible.

## Slide 8: Same price path, three responses
PICTURE THE NUMBERS
Chart: Year
| 2020 | 2030 | 2040 | 2050
Model A | 40 | 32 | 24 | 16
Model B | 40 | 34.7 | 29.3 | 24
Model C | 40 | 36 | 32 | 28
Illustrative models with straight-line paths, not real results
Read it like this
1
All three start at 40 Gt in 2020
2
In 2050: A 16, B 24, C 28 Gt
3
The spread starts an explanation; it is not a probability
Notes: This is the picture behind a diagnostic study: one standard test, many models. Ask what could make model C respond least. Possible answers: no carbon capture technology (structure), expensive solar (inputs), or no foresight (method). Each answer is a question to check in the model documentation.

## Slide 9: Worked example: a simple diagnostic indicator
WORKED EXAMPLE · STEP BY STEP
Problem Three models start at 40 Gt in 2020. Under the same price, in 2050 A emits 16, B 24 and C 28 Gt. How much does each cut?
1
Cut = (2020 value − 2050 value) ÷ 2020 value
2
A: (40 − 16) ÷ 40 = 24 ÷ 40 = 60%
3
B: (40 − 24) ÷ 40 = 16 ÷ 40 = 40%
4
C: (40 − 28) ÷ 40 = 12 ÷ 40 = 30%
5
A responds 60 ÷ 30 = 2 times as strongly as C
Answer Cuts of 60%, 40% and 30%: A responds twice as strongly as C
Notes: The percentage cut under a standard price is one of the diagnostic indicators researchers use. Harmsen and colleagues applied six indicators to 17 models and found large differences, even between versions of the same model; check those counts against the paper before teaching. The next question is never a number: it is why.

## Slide 10: Quick check
QUICK CHECK · THINK, THEN VOTE
12 of 18 models show fast solar growth. What can you conclude?
A
Fast solar growth is 67% likely
B
Most models behave that way under these assumptions
C
The other 6 models are wrong
D
Solar growth is certain
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: most models behave that way under the agreed assumptions. Models are not independent draws: many share data, assumptions and even code. A count across models describes the tools, not the probability of the outcome. This is the same warning as week 6 about bands on scenario charts.

## Slide 11: Quick check: answer
QUICK CHECK · ANSWER
12 of 18 models show fast solar growth. What can you conclude?
A
Fast solar growth is 67% likely
B
Most models behave that way under these assumptions
C
The other 6 models are wrong
D
Solar growth is certain
Notes: Answer: most models behave that way under the agreed assumptions. Models are not independent draws: many share data, assumptions and even code. A count across models describes the tools, not the probability of the outcome. This is the same warning as week 6 about bands on scenario charts.

## Slide 12: Worked example: match the units before comparing
WORKED EXAMPLE · STEP BY STEP
Problem GCAM reports a world total of 10,000 MtC (million tonnes of carbon). AR6 reports GtCO2. Convert.
1
A CO2 molecule weighs 44; its carbon atom weighs 12
2
So 1 tonne of carbon = 44 ÷ 12 = 3.667 tonnes of CO2
3
10,000 MtC × 44 ÷ 12 = 36,667 MtCO2
4
36,667 ÷ 1,000 = 36.7 GtCO2
Answer
10,000 MtC = 36.7 GtCO2
Notes: Forget the 44 over 12 and your GCAM line sits at about a quarter of every other model. Also match the scope: GCAM's query covers energy and industry, not land use, so compare with the AR6 variable Emissions|CO2|Energy and Industrial Processes. Both checks are built into the lab 12 helper function.

## Slide 13: What one big comparison found: EMF 27
KEY POINTS
18 energy-economy and integrated models ran the same technology and climate scenarios
They agreed on efficiency, electrification and fast clean-up of power
They found transport and other non-electric uses hardest to clean up
They found bioenergy and carbon capture especially valuable
Agreement and disagreement are both findings
Notes: EMF 27 was a study of the Stanford Energy Modeling Forum; its overview paper is Kriegler et al. (2014). These findings are quoted from memory of that overview, so check them against the source before teaching. Use the last finding as a hook for week 14, where heavy reliance on bioenergy and carbon capture is criticised.

## Slide 14: From a messy script to a reproducible analysis
COMPARE
Works on my laptop today
One long script with copied code blocks
Relies on objects left in the console
Files named final2_​really_​final.R
Anyone can rerun it
Functions live in the R folder and are sourced
Runs in a fresh session (Session, Restart R)
Every change saved as a Git commit with a message
Notes: Comparing your run with others is only useful if someone else can repeat it. The rule to teach: functions live in R, scripts in labs only load, call and plot. Restarting R is the real test, because a script that only works in a used session is not reproducible. The project hand-in uses exactly this test.

## Slide 15: Common mix-ups
WATCH OUT
Not quite
Better
Most models show X, so X is likely
Models share data and code. A spread describes the tools, not the odds.
Compare GCAM's MtC directly with AR6's MtCO2
Multiply by 44/12 first, and compare energy-and-industry CO2 with the same scope.
A model that disagrees with the others is broken
It may have a different structure, input or method. Find out which before judging.
Notes: The first two mistakes appear in almost every first draft of the lab 12 worksheet. The third matters for the explain-a-paper talks: an outlier model is often the most informative one.

## Slide 16: Words to add to the class glossary
NEW WORDS THIS WEEK
Model intercomparison A project where many modelling teams run the same agreed scenarios and report results in one shared format, so differences can be explained.
Model structure How a model is built: which regions, sectors and technologies exist and how they connect. It is fixed in the code.
Diagnostic indicator A standard number recorded for every model under the same test, such as how much emissions fall under one carbon price path.
Reproducible analysis An analysis that anyone can rerun from the folder of files and scripts and get the same tables and figures.
Git A tool that saves snapshots (commits) of your files with a short message, so you can see and undo every change.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 17: Lab 12: your GCAM run among AR6 scenarios
HANDS-ON LAB
Turn repeated code into two functions, place your CarbonPrice run among AR6 scenarios with a similar carbon price, and save the work with Git.
Script: labs/lab12.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. Turn repeated code into two functions, place your CarbonPrice run among AR6 scenarios with a similar carbon price, and save the work with Git. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 18: Turn the lab 6 reshape into a function
LAB · STEP 1 OF 4
to_long gives any AR6 variable in long form. Fill GAP 1 with the function's argument, then move the block to R/ar6_helpers.​R.
to_long <- function(ar6, variable) {
ar6 |>
filter(Variable == ___) |> # GAP 1
pivot_longer(matches("^[0-9]{4}$"),
names_to = "year", values_to = "value") |>
mutate(year = as.integer(year)) |>
drop_na(value)
}
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: The gap is variable. Students then move get_co2 to R/gcam_helpers.R in the same way and uncomment the two source() lines at the top of the script. The complete version is solutions/lab12_solution.R with the two helper files.

## Slide 19: Read GCAM's CO2 in GtCO2
LAB · STEP 2 OF 4
get_co2 sums all regions and converts million tonnes of carbon to GtCO2 with 44/12 and a division by 1,000.
get_co2 <- function(prj, scen) {
getQuery(prj, "CO2 emissions by region",
scenarios = scen) |>
group_by(scenario, year) |>
summarise(gt = sum(value) * 44 / 12 / 1000,
.groups = "drop")
}
prj <- loadProject("output/gcam_course.dat")
gcam <- get_co2(prj, "CarbonPrice")
Notes: Check before the session that the project file holds this query for every region, not only the example region. If the GCAM line later sits far below all AR6 lines, the 44/12 conversion or the sum over regions is missing.

## Slide 20: Pick AR6 runs with a similar price
LAB · STEP 3 OF 4
Choose a band around your 2050 carbon price, for example half to double. Fill GAPS 2 and 3.
similar <- to_long(ar6, "Price|Carbon") |>
filter(year == 2050,
value > ___, value < ___) # GAPS 2, 3
nrow(similar) # aim for 20 to 100
ar6_co2 <- to_long(ar6, co2_var) |>
semi_join(similar, by = c("Model", "Scenario")) |>
mutate(run = paste(Model, Scenario))
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: Give students the 2050 price of the CarbonPrice run in the unit of the AR6 variable, since GCAM reports prices in different units. co2_var is Emissions|CO2|Energy and Industrial Processes, to match the scope of the GCAM query.

## Slide 21: Save your work with Git
LAB · STEP 4 OF 4
Type these in the Terminal pane, not the Console. Copy gitignore_​lab12.txt to .gitignore first.
git init
git status
git add .gitignore R labs
git commit -m "write your own message here"
git log --oneline
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: The commit message should say what changed, for example Move AR6 and GCAM helpers into R folder. .gitignore keeps databases, project files and the output folder out of Git; it must be in place before the first git add, because files already tracked are not affected.

## Slide 22: Did it work?
LAB · CHECK YOUR WORK
You should see
nrow(similar) gives 20 to 100 scenarios
Your orange GCAM line sits among the grey AR6 lines, not at a quarter of them
git log --oneline shows your commit
Worksheet questions
1
Is your 2050 CO2 inside the AR6 range for a similar carbon price? Give the numbers.
2
Give two reasons from structure, inputs or method why your GCAM run could differ from the AR6 median.
3
Which files did you leave out of Git, and why?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 23: Take-home messages
RECAP
1
Models differ because of structure, inputs and method
2
Intercomparison projects fix inputs and a reporting format so the spread can be explained
3
A spread across models describes the tools, not the probability of an outcome
4
Match units (× 44/12) and scope before comparing GCAM with AR6
5
Functions in sourced files plus Git commits make an analysis reproducible
Next: week 13
Week 13 runs GCAM many times on purpose, and uses a decision tree to discover which assumptions lead to high emissions.
Practise
Interactive course, week 12: try the disagree explorer and the 5-question quiz.
Readings: Keppo et al. (2021), Exploring the possibility space, Environmental Research Letters; IPCC AR6 Working Group III, Annex III; GCAM v8.2 documentation: Emissions outputs, Community guidelines for articles using GCAM
Notes: Go back to the goals from the start: Name the three sources of difference: structure, inputs and method; Explain how an intercomparison project makes model results comparable; Compare a GCAM run with AR6 scenarios after matching units and scope; Organise an analysis into sourced functions and save it with Git. Ask students to rate themselves on each. Then point to next week: Week 13 runs GCAM many times on purpose, and uses a decision tree to discover which assumptions lead to high emissions.