## Slide 1: Uncertainty and scenario discovery
WEEK 13 OF 15 · STAGE 3: ADVANCED METHODS
One run is one guess; many runs show what matters
New R skill Batch runs; scenario discovery with a classification tree (rpart)
Modelling Climate and Energy Futures · beginner-friendly lecture and lab slides
Notes: Welcome to week 13: Uncertainty and scenario discovery. One run is one guess; many runs show what matters. Today has two halves: a lecture that builds the idea step by step with everyday examples, then a guided lab where we try it in R. Nobody is expected to know the material already. New R skill this week: Batch runs; scenario discovery with a classification tree (rpart).

## Slide 2: Where we are in the course
COURSE MAP
Stage 1
Foundations
Week 1
Why model the future?
Week 2
Climate primer
Week 3
Energy primer
Week 4
Economics primer
Week 5
Cost-benefit IAMs: DICE
Week 6
The scenario framework
Stage 2
GCAM in depth
Week 7
Inside GCAM
Week 8
Energy in GCAM
Week 9
Land, water and bioenergy
Week 10
Emissions and policy
Stage 3
Advanced methods
Week 11
Optimisation IAMs
Week 12
Why models disagree
Week 13
Uncertainty
Week 14
Frontiers and limits
Week 15
Projects and review
Notes: This is week 13 of 15. The course climbs in three stages: foundations (weeks 1 to 6), GCAM in depth (weeks 7 to 10) and advanced methods (weeks 11 to 15). Point out what came just before this week and what it prepares for, so students see each week as one step on a path rather than an isolated topic.

## Slide 3: By the end of today you can
TODAY'S GOALS
1
Name three kinds of uncertainty and how each is explored
2
Count the runs in an ensemble and explain why they grow so fast
3
Use a classification tree to find which inputs lead to high emissions
4
Explain robust decisions and emulators in plain words
Big question We do not know future solar costs, population or policy. How can a model help us decide anything when its inputs are so uncertain?
Notes: Read the goals aloud and ask students to keep them in mind. We come back to them on the recap slide at the end. Big question for today: We do not know future solar costs, population or policy. How can a model help us decide anything when its inputs are so uncertain?

## Slide 4: Write the scenario after the runs
LET'S START WITH A QUESTION
Usually you invent a scenario and then run the model. Today we run the model dozens of times first, and let the computer tell us which combinations of assumptions lead to trouble.
What would you want to know before trusting a single model run?
Notes: After the explain-a-paper talk, remind students of the week 5 lab where they ran DICE with different discount rates. That was their first sensitivity analysis. Today adds a way to make sense of many runs at once. Quiz 3 is this week, so keep time for it.

## Slide 5: Three kinds of uncertainty, three ways to explore them
SIDE BY SIDE
Kind | Example | How to explore it
Inputs | Future solar cost | Sensitivity runs, ensembles (today)
Model structure | Models built differently | Compare models (week 12)
Future society | Population, growth, policy | Scenarios such as the SSPs (week 6)
Your project's sensitivity test usually covers inputs; say what it leaves out
Notes: Inputs are numbers we could in principle measure better. Structure is only revealed by comparing models. The future of society is not a measurement problem at all, which is why scenarios are stories, not forecasts. Ask each team which kind its sensitivity test addresses.

## Slide 6: Weather forecasters never trust one run
AN EVERYDAY PICTURE
A weather service runs its forecast model many times with slightly different starting conditions. If 45 of 50 runs bring rain, you take an umbrella. If they split, you know the forecast is shaky. One run alone would hide that.
What it means for models
1
Many runs show how stable a result is
2
An ensemble varies several inputs together
3
But our inputs are chosen, not random draws
Notes: The analogy works for the idea of looking at a spread. Point out the limit at once: a weather ensemble samples measured uncertainty, while our ensemble uses values we chose to try. So in our case the share of runs is not a probability. This becomes a trap on a later slide.

## Slide 7: Worked example: counting ensemble runs
WORKED EXAMPLE · STEP BY STEP
Problem The lab ensemble varies solar cost (2 values), CO2 storage (2), SSP (3) and carbon price (3). How many runs?
1
Every combination: 2 × 2 × 3 × 3
2
2 × 2 = 4, then 4 × 3 = 12, then 12 × 3 = 36 runs
3
Add a fifth input with 3 values: 36 × 3 = 108 runs
4
At 2 hours a run, 4 runs at once: 108 × 2 ÷ 4 = 54 hours
Answer
36 runs in the lab; 108 runs and about 54 hours with one more input
Notes: Run times are illustrative. Each new input multiplies the count, which is why ensembles are designed with care and why large studies sample combinations instead of running all of them. Lamontagne and colleagues ran 33,750 GCAM scenarios in a 2018 study; check that number against the paper before teaching.

## Slide 8: Scenario discovery in four steps
HOW IT WORKS
1
Run many cases
Inputs differ: price, solar cost, CO2 storage, SSP
2
Label each run
High emissions in 2050: yes or no?
3
Fit a tree
It splits runs by input values
4
Read the leaves
Which settings lead to trouble?
Bryant and Lempert introduced the idea; Lamontagne et al. (2018) applied it to a large GCAM ensemble
Notes: Bryant and Lempert used a related algorithm called PRIM; a classification tree is simpler and enough for this course. Stress step 2: the label is a modelling choice. Move the cut-off and the discovered scenario can change, which the worksheet asks students to test.

## Slide 9: Worked example: growing a tree by hand
WORKED EXAMPLE · STEP BY STEP
Problem Eight runs; three are labelled HIGH. Which input settings explain them?
1
Split on carbon price. Low price: 4 runs, 3 HIGH. High price: 4 runs, 0 HIGH
2
That is a clean split, so carbon price comes first
3
Split the low-price group on solar cost. Solar high: 2 runs, both HIGH
4
Solar low: 2 runs, 1 HIGH
5
Rule: low carbon price AND high solar cost → HIGH
6
The rule is right on 7 of 8 runs = 87.5%
Answer Low carbon price with high solar cost leads to high emissions (right on 7 of 8)
Notes: Illustrative runs. A classification tree does exactly this: at each step it picks the input split that best separates HIGH from the rest. Read the result aloud as a sentence; that sentence is the discovered scenario. Remind students that the tree describes the model's behaviour, not cause and effect in the real world.

## Slide 10: Quick check
QUICK CHECK · THINK, THEN VOTE
In the lab, 9 of 36 runs are labelled high. What does that tell you?
A
There is a 25% chance of high emissions
B
Under the values we chose, a quarter of runs end high
C
The other 27 runs are wrong
D
High emissions are unlikely
Notes: Give students 30 seconds to think and vote with fingers (1 to 4) before showing the next slide. Answer: it describes the runs under the values we chose to try. Pick different values and the share changes. An ensemble shows the spread of outcomes, not their likelihood. This is the most common error in worksheet 12.

## Slide 11: Quick check: answer
QUICK CHECK · ANSWER
In the lab, 9 of 36 runs are labelled high. What does that tell you?
A
There is a 25% chance of high emissions
B
Under the values we chose, a quarter of runs end high
C
The other 27 runs are wrong
D
High emissions are unlikely
Notes: Answer: it describes the runs under the values we chose to try. Pick different values and the share changes. An ensemble shows the spread of outcomes, not their likelihood. This is the most common error in worksheet 12.

## Slide 12: Robust choice: keep the worst regret small
SIDE BY SIDE
Strategy | Future 1 | Future 2 | Future 3 | Worst regret
A: rely on one technology | 100 | 110 | 200 | 200 − 125 = 75
B: spread across several | 115 | 118 | 125 | 115 − 100 = 15
Best in each future | 100 | 110 | 125 | 
Cost to meet a target, index. Regret = your cost − the best cost in that future. Illustrative.
Notes: Work it through: A's regrets are 0, 0 and 75; B's are 15, 8 and 0. A least-cost model that trusts future 1 picks A. A robust analysis picks B, whose worst regret is five times smaller. Robust decision making was developed at RAND by Lempert, Popper and Bankes. Link to week 11: perfect foresight is the purest form of betting on one future.

## Slide 13: Two more tools for a very uncertain future
KEY IDEA
1
Emulators
A fast stand-in for a slow model. Week 2's rule, 0.45 °C per 1,000 GtCO2, is an emulator of full climate models.
2
Robust decision making
Examine a very wide range of futures and look for near-term choices that hold up in nearly all of them.
3
Why they matter
Thousands of runs need cheap runs; good decisions need to survive the futures we did not expect.
Notes: Emulators exist because large models are slow. Students have already met one: Hector stands in for big Earth system models, and AR6 used climate emulators to assign temperatures to scenarios; check that description against AR6 before teaching. Keep this slide brief; the aim is recognition.

## Slide 14: Common mix-ups
WATCH OUT
Not quite
Better
9 of 36 runs are high, so there is a 25% chance
The share depends on the values you chose to try. It is not a probability.
The tree shows what causes high emissions in the real world
It describes how this model behaves across these runs, nothing more.
A tree that fits every run perfectly is the best tree
It may just memorise the runs. Keep it small and check its accuracy.
Notes: All three appear in quizzes and worksheets. The third is the beginning of an idea called overfitting; students do not need the word, only the habit of preferring a short tree they can read as one sentence.

## Slide 15: Words to add to the class glossary
NEW WORDS THIS WEEK
Sensitivity analysis Changing one input at a time, holding the rest fixed, to see how far the result moves. You did this with DICE in week 5.
Ensemble A set of model runs that changes several inputs together, running every combination or a sample of them.
Scenario discovery Running many cases first, labelling the outcomes you care about, then letting a computer find which input settings lead to them.
Emulator A fast, simple formula fitted to a slow model's runs, so thousands of cases can be tried in seconds.
Robust decision A choice that works acceptably across many possible futures, instead of being best in one.
Notes: These are the only new terms this week. Ask two students to read them aloud and add them to the shared class glossary. If any definition is unclear, rewrite it together in plainer words; that rewriting is part of learning it.

## Slide 16: Lab 13: an ensemble and scenario discovery
HANDS-ON LAB
See how a 36-run GCAM ensemble was set up, label the high-emission runs and let a classification tree find which inputs lead to them.
Script: labs/lab13.R
4 steps
Stuck? Read the error aloud, check the slide, then ask
Notes: Lab time. See how a 36-run GCAM ensemble was set up, label the high-emission runs and let a classification tree find which inputs lead to them. Open the course project in RStudio first so file paths work. Rule for getting stuck: read the error message aloud to a neighbour, check the "you should see" slide, then raise a hand.

## Slide 17: Read the batch file (no code)
LAB · STEP 1 OF 4
1
Open gcam-files/ensemble_​batch.xml. Each ComponentSet is one input; GCAM runs every combination: 2 × 2 × 3 × 3 = 36.
Notes: A GCAM ensemble takes hours, so the instructor made the runs before the session. Walk through the four inputs: solar cost, CO2 storage, SSP and carbon price. Batch mode is documented in the GCAM user guide: set BatchMode to 1, name the batch file under Files, and GCAM runs every combination of the file sets. Our batch file has not been run; its header lists what to check against the installed release.

## Slide 18: Load the results
LAB · STEP 2 OF 4
One row per run. rpart wants text columns as factors, so convert them.
library(tidyverse)
library(rpart)
ens <- read_csv("data/ensemble_results.csv") |>
mutate(across(where(is.character), factor))
glimpse(ens)
count(ens, solar_cost, ccs_storage,
ssp, carbon_price) # 36 rows, n = 1
Type it rather than paste it, run one line at a time (Ctrl+Enter), and check the output before the next line.
Notes: The column names are the course's own choice; gcam-files/ensemble_configuration_changes.txt explains how the instructor builds this file from the 36 runs.

## Slide 19: Label the high-emission runs
LAB · STEP 3 OF 4
A run is high if its 2050 CO2 is above a cut-off you choose. Fill GAP 1: 0.75 marks the top quarter.
cut_off <- quantile(ens$co2_2050, ___) # GAP 1
ens <- ens |>
mutate(high = factor(if_else(
co2_2050 > cut_off, "high", "other")))
count(ens, high)
Fill each ___ gap before running that line. Stuck? The solution file has the complete version.
Notes: With 0.75 about 9 of 36 runs are high. The cut-off is a judgement; the worksheet asks what happens when it moves to 0.5. The script also draws a histogram of 2050 emissions coloured by label, worth showing before the tree.

## Slide 20: Fit the tree and read it
LAB · STEP 4 OF 4
The tree splits runs on one input at a time. Fill GAP 2 with "class" so predict returns labels.
tree <- rpart(high ~ solar_cost + ccs_storage +
ssp + carbon_price,
data = ens, method = "class",
minsplit = 6)
plot(tree, margin = 0.1)
text(tree, use.n = TRUE, pretty = 0)
ens <- ens |>
mutate(pred = predict(tree, type = ___)) # GAP 2
mean(ens$pred == ens$high)
Notes: minsplit = 6 lets the tree split small groups. A run goes left when the condition at the split is true. The expected pattern is carbon price first and the SSP second, but confirm on your own file before the session. The complete script is solutions/lab13_solution.R.

## Slide 21: Did it work?
LAB · CHECK YOUR WORK
You should see
count(ens, high) shows about 9 high and 27 other
The tree's first split is on an input you can name
The share of runs the tree gets right is printed
Worksheet questions
1
Read one path from the top of your tree to a high leaf as a sentence.
2
Which input does the tree use first? Is that what you expected, and why?
3
Change the cut-off to 0.5 and fit the tree again. Does the first split stay the same? What does that say about the label?
Notes: Leave this slide up for the last twenty minutes. Students compare their output with the left column, then start the worksheet questions on the right. Anyone whose results differ should compare their code with a neighbour line by line.

## Slide 22: Take-home messages
RECAP
1
Uncertainty comes from inputs, model structure and the future of society
2
Ensembles vary several inputs together; every new input multiplies the number of runs
3
Scenario discovery labels runs and fits a tree to find the settings that lead to trouble
4
A share of runs is not a probability, and a tree describes the model, not the world
5
Robust choices keep the worst regret small; emulators make many runs affordable
Next: week 14
Week 14 looks at where IAMs are heading and at the main criticisms of them, and turns your draft results into clear figures.
Practise
Interactive course, week 13: try the ensemble explorer and the 5-question quiz.
Readings: Lamontagne et al. (2018), Large ensemble analytic framework for consequence-driven discovery of climate change scenarios, Earth's Future; rpart package documentation; GCAM v8.2 documentation: How to Get Started (batch mode), Shared Socioeconomic Pathways
Notes: Go back to the goals from the start: Name three kinds of uncertainty and how each is explored; Count the runs in an ensemble and explain why they grow so fast; Use a classification tree to find which inputs lead to high emissions; Explain robust decisions and emulators in plain words. Ask students to rate themselves on each. Then point to next week: Week 14 looks at where IAMs are heading and at the main criticisms of them, and turns your draft results into clear figures.